## Slide 1: Network+ Guide to Networks Eighth Edition
Chapter 1
Introduction to Networking
© 2019 Cengage. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Objectives (1 of 2)
1.1 Distinguish between the client-server and peer-to-peer models used to control access to a network
1.2 Identify types of applications and protocols used on a network
1.3 Describe various networking hardware devices and the most common physical topologies

## Slide 3: Objectives (2 of 2)
1.4 Describe the seven layers of the O S I model
1.5 Explain best practices for safety when working with networks and computers
1.6 Describe the seven-step troubleshooting model for solving a networking problem

## Slide 4: Network Models
Topology—How parts of a whole work together
Physical topology—Mostly applies to hardware and describes how computers, other devices, and cables fir together to form the physical network
Logical topology—Has to do with software and describes how access to the network is controlled
  How users and programs initially gain access to the network
Network operating system (N O S)—Controls access to the entire network
  Required by client-server models

## Slide 5: Peer-to-Peer Network Model (1 of 3)
Peer-to-peer (P 2 P) network model—The O S of each computer on the network is responsible for controlling access to its resources
  No centralized control
Computers, called nodes or hosts, form a logical group of computers and users
  May share resources
  May prevent access to resources
Each computer user has a Windows local account
  Works only on that one computer

## Slide 6: Peer-to-Peer Network Model (2 of 3)

## Slide 7: Peer-to-Peer Network Model (3 of 3)
Advantages
  Simple configuration
  Less expensive
    Compared to other network models
Disadvantages
  Not scalable
  Not necessarily secure
  Not practical for large installations

## Slide 8: Client-Server Network Model (1 of 5)
Resources are managed by the network operating system (N O S) via a centralized directory database
Windows domain—A logical group of computers that a Windows Server can control
Active Directory (A D)—The centralized directory database that contains user account information and security for the entire group of computers
A user can sign on to the network from any computer on the network and gain access to the resources that A D allows
  This process is managed by Active Directory Domain Services (A D D S)

## Slide 9: Client-Server Network Model (2 of 5)
Client
  A computer making a request from another
Clients don’t share their resources directly with each other
  Access is controlled by entries in the centralized domain database
Client computers access resources on another computer by way of the servers controlling the domain database

## Slide 10: Client-Server Network Model (3 of 5)

## Slide 11: Client-Server Network Model (4 of 5)
The N O S is responsible for the following activities:
  Manages client data, resources
  Ensures authorized user access
  Controls user file access
  Restricts user network access
  Dictates computer communication rules
  Supplies application to clients
Server examples
  Windows Server 2016, Ubuntu Server, or Red Hat Enterprise Linux

## Slide 12: Client-Server Network Model (5 of 5)
Servers that have a N O S installed require:
  More memory, processing, and storage capacity
  Equipped with special hardware
    Provides network management functions
Advantages relative to peer-to-peer networks
  User credential assigned from one place
  Multiple shared resource access centrally controlled
  Central problem monitoring, diagnostics, and correction capabilities
  More scalable

## Slide 13: Client-Server Applications (1 of 5)
Network services—The resources a network makes available to its users
  Includes applications and the data provided by these applications
In client-server applications
  A client computer requests data or a service from a second computer, called the server
Protocols
  Methods and rules for communication between networked devices
Two primary protocols:
  T C P (Transmission Control Protocol)
  I P (Internet Protocol)
  T C P/I P suite of protocols is used by O Ss for communication on a network

## Slide 14: Client-Server Applications (2 of 5)

## Slide 15: Client-Server Applications (3 of 5)
List of several popular client-server applications:
  Web service
  Email services
  F T P service
  Telnet service
  Remote applications
  Remote Desktop

## Slide 16: Client-Server Applications (4 of 5)

## Slide 17: Client-Server Applications (5 of 5)

## Slide 18: Network Hardware (1 of 9)
Local area network (LAN)—Usually contained in a small space
  Such as an office or building
Switch—Receives incoming data from one of its ports and redirects it to another port or multiple ports
  Will send the data to its intended destination
Star topology—All devices connect to one central device (usually a switch)
Network interface card (N I C)—A network port used to attach a device to a network

## Slide 19: Network Hardware (2 of 9)

## Slide 20: Network Hardware (3 of 9)

## Slide 21: Network Hardware (4 of 9)

## Slide 22: Network Hardware (5 of 9)
A LAN can have several switches
Backbone—A central conduit that connects the segments (pieces) of a network
  Might use higher transmission speeds and different cabling than network cables connected to computers
Three switches daisy-chained together in a single line is said to use a bus topology
  However, each switch is connected to computers via a star topology, making it a star-bus topology
  A topology that combines topologies is known as a hybrid topology

## Slide 23: Network Hardware (6 of 9)

## Slide 24: Network Hardware (7 of 9)
Router—A device that manages traffic between two or more networks
  Can help find the best path for traffic to get from one network to another
Routers can be used in small home networks to connect the home LAN to the Internet
  Called a S O H O (small office-home office) network
Industrial-grade routers can have several network ports, one for each network it connects to
Difference between router and switch:
  Router is like a gateway between networks and belongs to two or more local networks
  Switch belongs only to its local network

## Slide 25: Network Hardware (8 of 9)

## Slide 26: Network Hardware (9 of 9)

## Slide 27: MANs and WANs (1 of 2)
Metropolitan area network (MAN)—A group of connected LANs in the same geographical area
  Also known as a campus area network (CAN)
WAN (wide area network)—A group of LANs that spread over a wide geographical area
  Internet is the largest and most varied WAN
MANs and WANs often use different transmission methods and media than LANs
PAN (personal area network)—Smallest network
  A network of personal devices such as your smartphone and your computer

## Slide 28: MANs and WANs (2 of 2)

## Slide 29: The Seven-Layer O S I Model (1 of 3)
Compare two devices communicating on a network to two people communicating by way of the U.S. Postal Service

## Slide 30: The Seven-Layer O S I Model (2 of 3)
O S I (Open Systems Interconnection) reference model—A seven-layer model developed to categorize the layers of communication
The layers are numbered in order, starting with Layer 1, the Physical layer at the bottom
  Physical, Data Link, Network, Transport, Session, Presentation, Application

## Slide 31: The Seven-Layer O S I Model (3 of 3)

## Slide 32: Layer 7: Application Layer
Application layer—Describes the interface between two applications, on separate computers
Application layer protocols are used by programs that fall into two categories:
  Provide services to a user, such as a browser and Web server
  Utility programs that provide services to the system, such as S N M P that monitor and gather information about network traffic
Payload—Data that is passed between applications or utility programs and the O S

## Slide 33: Layer 6: Presentation Layer
Presentation layer—Responsible for reformatting, compressing, and/or encrypting data in a way that the receiving application can read
Example:
  An email message can be encrypted at the Presentation layer by the email client or by the O S

## Slide 34: Layer 5: Session Layer
Session layer—Describes how data between applications is synched and recovered if messages don’t arrive intact at the receiving application
The Application, Presentation, and Session layers are intertwined
  Often difficult to distinguish between them
Most tasks are performed by the O S when an application makes an A P I call to the O S
  Application programming interface (A P I) call is the method an application uses when it makes a request of the O S

## Slide 35: Layer 4: Transport Layer (1 of 2)
Transport layer—Responsible for transporting Application layer payloads from one application to another
Two main Transport layer protocols are:
  T C P (Transmission Control Protocol)—Makes a connection with the end host, checks whether data was received; called a connection-oriented protocol
  U D P (User Datagram Protocol)—Does not guarantee delivery by first connecting and checking whether data is received; called a connectionless protocol

## Slide 36: Layer 4: Transport Layer (2 of 2)
Protocols add their own control information in an area at the beginning of the payload (called a header)
Encapsulation—Process of adding a header to the data inherited from the layer above
The Transport layer header addresses the receiving application by a number called a port number
If message is too large, T C P divides it into smaller messages called segments
  In U D P, the message is called a datagram

## Slide 37: Layer 3: Network Layer
Network layer—Responsible for moving messages from one node to another until they reach the destination host
I P adds its own Network layer header to the segment or datagram
  The entire Network layer message is called a packet
I P address—Assigned to each node on a network
  Network layer uses it to uniquely identify each host
I P relies on several routing protocols to find the best route for a packet to take to reach destination
  I C M P and A R P are examples
Network layer protocol will divide large packets into smaller packets
  Process called fragmentation

## Slide 38: Layer 2: Data Link Layer (1 of 2)
Layers 2 and 1 are responsible for interfacing with physical hardware on the local network
  Protocols at these layers are programmed into firmware of a computer’s N I C and other hardware
Type of networking hardware or technology used on a network determine the Link Layer protocol used
  Ethernet and Wi-Fi are examples
The Link layer puts control information in a Link layer header and at the end of the packet in a trailer
  Entire Link layer is called a frame

## Slide 39: Layer 2: Data Link Layer (2 of 2)
MAC (Media Access Control) address—Hardware address of the source and destination N I Cs
  Also called a physical address, hardware address, or Data Link layer address
  Embedded on every network adapter and are considered short-range addresses that can only find nodes on the local network

## Slide 40: Layer 1: Physical Layer
Physical layer—Simplest layer and is responsible for sending bits via a wired or wireless transmission
Can be transmitted as:
  Wavelengths in the air
  Voltage on a copper wire
  Light (via fiber-optic cabling)

## Slide 41: Protocol Data Unit or P D U
Protocol data unit (P D U)—The technical name for a group of bits as it moves from one layer to the next and from one LAN to the next
  Technicians loosely call this group of bits a message or a transmission
Table 1-1 Names for a P D U or message as it moves from one layer to another
OSI model | Name | Extremely technical name
Layer 7, Application layer Layer 6, Presentation layer Layer 5, Session layer | Payload or data | L7P D U
Layer 4, Transport layer | Segment (T C P) or datagram (U D P) | L4P D U
Layer 3, Network layer | Packet | L3P D U
Layer 2, Data Link layer | Frame | L2P D U
Layer 1, Physical layer | Bit or transmission | L1P D U

## Slide 42: Summary of How the Layers Work Together

## Slide 43: Safety Procedures and Policies
Network and computer technicians need to know how to protect themselves
  As wells as protect sensitive electronic components
This section takes a look at some best practices for safety

## Slide 44: Emergency Procedures (1 of 2)
Know the best escape route or emergency exit
Fire Suppression Systems—Have a fire suppression system in the data center that includes:
  Emergency alert system
  Portable fire extinguishers
  Emergency power-off switch
  Suppression agent
Fail Open or Fail Close—Does the security system allow access during a failure (fail open) or deny access during the failure (fail close)

## Slide 45: Emergency Procedures (2 of 2)
Material Safety Data Sheet (M S D S)—Explains how to properly handle substances such as chemical solvents and how to dispose of them
  Includes information such as physical data, toxicity, health effects, first aid, storage, shipping, disposal, and spill procedures

## Slide 46: Safety Precautions (1 of 5)
Electrical and tool safety is generally regulated by O S H A (Occupational Safety and Health Administration)
O S H A guidelines when using power tools:
  Wear personal protective equipment (P P E)
  Keep all tools in good condition and properly store tools not in use
  Use the right tool for the job and operate the tool according to the manufacturer’s instructions
  Watch out for trip hazards, so you and others don’t stumble on a tool or cord

## Slide 47: Safety Precautions (2 of 5)
Lifting heavy objects—Follow these guidelines:
  Decide which side of object to face so load is most balanced
  Stand close to the object with your feet apart
  Keep your back straight, bend knees and grip load
  Lift with your legs, arms, and shoulders (not your back or stomach)
  Keep the load close to your body and avoid twisting your body while you’re holding it
  To put the object down, keep your back as straight as possible and lower object by bending your knees

## Slide 48: Safety Precautions (3 of 5)
Protecting against static electricity:
  Computer components are grounded inside a computer case
  Grounding means that a device is connected directly to the earth
Sensitive electronic components can be damaged by electrostatic discharge (E S D)
Static electricity can cause two types of damage:
  Catastrophic failure—destroyed beyond use
  Upset failure—shorten the life of a component

## Slide 49: Safety Precautions (4 of 5)
Before touching a component, ground yourself by:
  Wearing an E S D strap around your wrist that clips onto the chassis or computer case
  Touching the case before touching any component inside the case
  Storing a component inside an antistatic bag
In addition to protecting against E S D, always shut down and unplug a computer before working inside it

## Slide 50: Safety Precautions (5 of 5)

## Slide 51: Troubleshooting Network Problems (1 of 2)
Troubleshooting steps used by most expert networking troubleshooters:
  Identify problem
    Gather information
    Identify symptoms
    Question users
    Determine if anything has changed
  Establish theory of probable cause
    Question the obvious
  Test theory to determine cause
    If theory confirmed, determine next steps
    If theory not confirmed, establish new theory or escalate

## Slide 52: Troubleshooting Network Problems (2 of 2)
Troubleshooting steps used by most expert networking troubleshooters (continued):
  Establish action plan
  Implement solution or escalate the problem
  Verify full functionality
    Implement preventative measures if applicable
  Document findings, actions, outcomes

## Slide 53: Chapter Summary (1 of 3)
The peer-to-peer model can be achieved using any assortment of desktop, mobile, or tablet O Ss
Peer-to-peer networks are simple to configure and less expensive than other types of networks
When Windows Server controls network access, the logical group is called a domain
Computers on a network are able to communicate with each other via the protocols they have in common
The fundamental difference between a switch and a router is that a switch belongs only to its local network and a router belongs to two or more local networks
A group of LANs spread over a wide geographical area is called a WAN (wide area network)

## Slide 54: Chapter Summary (2 of 3)
The Application layer describes the interface between two applications, each on separate computers
The Presentation layer is responsible for reformatting, compressing, and/or encrypting data in a way that the application on receiving end can read
The Session layer describes how data between applications is synced and recovered if messages don’t arrive intact at the receiving application
The Transport layer transports Application layer payloads from one application to another
The Network layer moves messages from one node to another until they reach the destination host
Layers 2 and 1 are responsible for interfacing with the physical hardware only on the local network

## Slide 55: Chapter Summary (3 of 3)
In case of an emergency, you’ll need to know the best escape route or emergency exit for you and others around you
Whenever possible, put heavy objects on a cart to move them
When your body and a component have different static charges and you touch the component, you can discharge up to 1500 volts of static electricity without seeing a spark or feeling the discharge
  It only takes 10 volts to damage the component