## Slide 1: Network+ Guide to Networks Eighth Edition
Chapter 2
Network Infrastructure and Documentation
© 2019 Cengage. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Objectives
2.1 Identify and describe network and cabling equipment in commercial buildings and work areas
2.2 Create and analyze network diagrams
2.3 Explain operating procedures, inventory management, labeling conventions, and business documents for a typical network
2.4 Track the progress of changes made to a network

## Slide 3: Components of Structured Cabling
T I A/E I A’s joint 568 Commercial Building Wiring Standard:
  Also known as structured cabling
  Describes the best way to install networking media to maximize performance and minimize upkeep
  Apply no matter what type of media, transmission technology, or networking speeds are involved
  Based on hierarchical design and assumes a network is based on the star topology

## Slide 4: From the Demarc to a Workstation (1 of 10)

## Slide 5: From the Demarc to a Workstation (2 of 10)

## Slide 6: From the Demarc to a Workstation (3 of 10)
Data rooms, racks, and other equipment:
  Entrance facility—Incoming network (such as Internet) connects with the school or corporate network
  Demarc (demarcation point)—Device that marks where a telecommunications service provider’s network ends and the organization’s network begins
  M D F (main distribution frame/facility)—Centralized point of interconnection for an organization’s LAN or WAN (also called M C or main cross connect)
  Data room—Enclosed space that hold network equipment (also called data closet, data center, equipment room, or telecommunications room)
  Racks—Holds various network equipment
  Patch panel—Panel of data receptors that can be mounted to a wall or a rack
    Provides central termination point when many patch cables converge in a single location

## Slide 7: From the Demarc to a Workstation (4 of 10)

## Slide 8: From the Demarc to a Workstation (5 of 10)

## Slide 9: From the Demarc to a Workstation (6 of 10)
Data rooms, racks, and other equipment (continued):
  V o I P telephone equipment—Voice over I P is the use of any network to carry voice signals using T C P/I P protocols
    V o I P gateway
    V o I P P B X
    V o I P endpoints
  I D F (intermediate distribution frame)—Provides an intermediate connection between the M D F and end-user equipment on each floor and in each building
  Work area—Encompasses workstations, printers, and other network devices
  Wall jacks—T I A/E I A standard calls for each wall jack to contain at least one voice and one data outlet

## Slide 10: From the Demarc to a Workstation (7 of 10)

## Slide 11: From the Demarc to a Workstation (8 of 10)

## Slide 12: From the Demarc to a Workstation (9 of 10)

## Slide 13: From the Demarc to a Workstation (10 of 10)
Rack systems

## Slide 14: Cabling (1 of 6)
Types of cables:
  Patch cable—A relatively short length of cabling with connectors at both ends
  Horizontal cabling—Connects workstations to the closest data room and to switches housed in the room
  Backbone cabling—Consists of cables or wireless links that provide interconnection between the entrance facility and M D F and between M D F and I D Fs

## Slide 15: Cabling (2 of 6)

## Slide 16: Cabling (3 of 6)

## Slide 17: Cabling (4 of 6)

## Slide 18: Cabling (5 of 6)
Cable management:
  When terminating twisted-pair cabling, don’t leave more than 1 inch of exposed cable before a termination
  Do not exceed the cable’s prescribed bend radius (radius of the maximum arc into which you can loop a cable without impairing data transmission)
  Use a cable tester to verify continuity (each cable segment transmits data reliably)
  Cinch cables loosely
  Protect cables—avoid laying cables across a floor and use cord covers if they must be exposed
  Avoid E M I—Electromagnetic interference
  Make sure cable sheath is plenum-rated

## Slide 19: Cabling (6 of 6)
Cable management:
  Pay attention to grounding requirements
  Leave some slack in cable runs
  Use cable management devices such as cable trays, braided sleeving, and furniture grommets
  Use patch panels to organize and connect lines
  Use company standards and stock
  Documentation:
    Keep your cable plant documentation accessible
    Label every data jack or port, patch panel, and connector
    Use color-coded cables for different purposes
    Update your documentation as you make changes to the network

## Slide 20: Monitoring the Environment and Security
Data rooms are often serviced by H V A C systems that are separate from the rest of the building
Specialized products can monitor the critical factors of a data closet’s environment:
  Unacceptable temperature
  Humidity
  Airflow conditions
Every data room should be locked with only limited I T personnel having keys
  Security cameras are suggested

## Slide 21: Network Documentation
Having up-to-date and detailed documentation of your network is essential for the following reasons:
  Makes communication with coworkers more efficient
  Speeds up troubleshooting efforts
  Puts information at your fingertips when facing similar problems in the future

## Slide 22: Network Diagrams (1 of 7)
Network diagrams—Graphical representations of a network’s devices and connections
  May show physical layout, logical topology, I P address reserves, names of major network devices, and types of transmission media
Network mapping—The process of discovering and identifying the devices on a network:
  Nmap—One of the most popular tools used for network mapping
  Zenmap—N map’s G U I option
Cisco Systems set the standard for diagram symbols used to represent network devices

## Slide 23: Network Diagrams (2 of 7)

## Slide 24: Network Diagrams (3 of 7)

## Slide 25: Network Diagrams (4 of 7)

## Slide 26: Network Diagrams (5 of 7)
Network diagrams provide broad snapshots of a network’s physical or logical topology
  Useful for planning where to insert a new switch or determining how a particular router, gateway, or firewall interact
Wiring schematic—A graphical representation of a network’s wired infrastructure
  In detailed form, it shows every wire necessary to interconnect network devices
Rack diagram—Drawing that show devices stacked in a rack system

## Slide 27: Network Diagrams (6 of 7)

## Slide 28: Network Diagrams (7 of 7)

## Slide 29: Operating Procedures
Essential documentation:
  Logical and physical connections on a network
  Inventory management
  I P address utilization
  Vendors
  Internal operating procedures
  Policies
  Standards
An organization could provide an internal website or database to hold this information

## Slide 30: Inventory Management
System life cycle (S L C)—Process of designing, implementing, and maintaining an entire network
S L C includes:
  Removal and disposal of outdated assets
  Addition of compatible, updated devices
Inventory management—The monitoring and maintaining of all assets that make up a network:
  Simplifies maintaining and upgrading a network
  Provides network administrators with information about the costs and benefits of certain types of hardware or software

## Slide 31: Labeling and Naming Conventions (1 of 2)
Tips for labeling and naming conventions:
  Use names that are as descriptive as possible
  Only include fields that are essential in identifying the device
  Don’t overcomplicate the name with useless or redundant information
  Use established naming conventions
  Think big-picture-down-to-details
  Consider any security risks from details included in your naming convention
  Use color-coded cables for different purposes and use cable tags to identify each cable’s purpose
  Label the ports and jacks that cables connect to
  Where labels won’t fit on the device, draw a simple diagram of each device that indicates how each port is used
  Use a portable label maker and use labels that are durable and are designed to stick to plastic and metal

## Slide 32: Labeling and Naming Conventions (2 of 2)

## Slide 33: Business Documents (1 of 2)
Standard business documents you may encounter:
  R F P (request for proposal)
    Request to vendors to submit a proposal for a product or service your company wants to purchase
  M O U (memorandum of understanding)
    Documents the intentions of two or more parties to enter into a binding agreement, or contract
  S O W (statement of work)
    Documents in detail the work that must be completed for a particular project

## Slide 34: Business Documents (2 of 2)
Standard business documents you may encounter (continued):
  S L A (service-level agreement)
    A legally binding contract or part of a contract that defines the aspects of a service provided to a customer
    Example: The service provided by an I S P
  M S A (master service agreement)
    A contract that defines the terms of future contracts between parties
    Such as payment terms or arbitration arrangements
  M L A (master license agreement)
    Grants a license from a creator, developer, or producer to a third party for the purposes of marketing or sublicensing, or distributing the product to consumers

## Slide 35: Change Management
Managing change while maintaining network’s efficiency and availability:
  Requires good planning
  Network users need to know when to expect certain network resources to be unavailable
Common software and hardware changes
  Range from installing patches to replacing network backbone
You may also need to know the change management documentation that might be required for an enterprise-scale network

## Slide 36: Software and Hardware Changes (1 of 3)
Four types of changes to existing software:
  Patch
    A correction, improvement, or enhancement
  Upgrade
    A major change to a software package that enhances the functionality and features of the software
  Rollback
    Also called backleveling or downgrading
    Process of reverting to a previous version after attempting to patch or upgrade it
  Installation
    New software to be installed on relevant devices and incorporated with network resources
Hardware changes could include adding new security cameras, replacing workstations, installing new printers, and upgrading hardware

## Slide 37: Software and Hardware Changes (2 of 3)
Table 2-3 Reversing a software upgrade
Type of upgrade | Options for reversing
Operating system patch | Use the patch’s automatic uninstall utility
Client software upgrade | Use the upgrade’s automatic uninstall utility, or reinstall the previous version of the client on top of the upgrade
Shared application upgrade | Use the application’s automatic uninstall utility, or maintain a complete copy of the previous installation of the application and reinstall over the upgrade
Operating system upgrade | Prior to the upgrade, make a complete backup of the system; to roll back, restore the entire system from the backup; uninstall an operating system upgrade only as a last resort

## Slide 38: Software and Hardware Changes (3 of 3)
The same change management principles apply to any type of change:
  Process all changes through the proper channels
  Minimize negative impacts on business procedures
  Plan thoroughly to maximize the changes of a successful change on the first attempt
  Document each change throughout the process

## Slide 39: Change Management Documentation
Generally, the larger an organization, the more documentation required when making changes
Required process will vary but expect the following:
  Submit a change request document
  Understand and follow the approval process
  The change is project managed (change coordinator is usually assigned)
  Provide additional documentation that could include:
    Network configuration
    IP address utilization
    Additions to the network
    Physical location changes
  Close the change

## Slide 40: Chapter Summary (1 of 3)
Organizations tend to follow a single cabling standard known as T I A/E I A-568 Commercial Building Wiring Standard or structured cabling
A network begins at the demark and ends at a workstation
Horizontal cabling connects workstations to the closest data room and to switches housed in that room
  The backbone consists of the cables or wireless links that provide interconnection between the entrance facility and M D F, and between the M D F and I D Fs
Data rooms are often serviced by H V A C systems that are separate from the rest of the building
  Specialized products are available that monitor the critical factors of a data room’s environment

## Slide 41: Chapter Summary (2 of 3)
Network diagrams may show physical layout, logical topology, I P address reserves, names of major network devices, and types of transmission media
Inventory management simplifies maintaining and upgrading the network chiefly because you know what the system includes
The secret to keeping track of devices is naming them systematically and then labeling them with those names
It’s important to understand the specifics covered—and not covered—in a particular document before signing it
Four types of software changes include a patch, upgrade, rollback, and installation

## Slide 42: Chapter Summary (3 of 3)
Typical hardware changes include adding new security cameras, replacing old workstations, installing new printers, and upgrading I P phone hardware
Generally, the larger an organization, the more documentation is necessary when making hardware and software changes