## Slide 1: Network+ Guide to Networks Eighth Edition
Chapter 3
Addressing on Networks
© 2019 Cengage. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Objectives (1 of 2)
3.1 Find the MAC address of a computer and explain its function in network communications
3.2 Configure T C P/I P settings on a computer, including I P address, subnet mask, default gateway, and D N S servers
3.3 Explain the purpose of ports and sockets, and identify the ports of several common, network protocols

## Slide 3: Objectives (2 of 2)
3.4 Describe domain names and the name resolution process
3.5 Use command-line tools to troubleshoot problems with network addresses

## Slide 4: Addressing Overview
Four addressing methods:
  Data Link layer MAC address
    48 bits, written as six hex numbers separated by colons
    Also called physical address
  Network layer I P address
    I P v 4 addresses have 32 bits and are written as four decimal numbers called octets
    I P v 6 addresses have 128 bits and are written as eight blocks of hexadecimal number
  Transport layer port numbers
  Application layer F Q D Ns, computer names, and host names
    Fully qualified domain name (F Q D N)—A unique character-based name
© 2019 Cengage. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 5: MAC Addresses
Traditional MAC addresses contain two parts:
  First 24 bits are known as the O U I (Organizationally Unique Identifier) or manufacturer-I D
    Assigned by the I E E E
  Last 24 bits make up the extension identifier or device I D
    Manufacturers assign each N I C a unique device I D

## Slide 6: I P Addresses (1 of 2)
Static I P addresses are assigned manually by the network administrator
Dynamic I P addresses are automatically assigned by a D H C P (Dynamic Host Configuration Protocol) server
  You’ll learn more about D H C P later in the chapter
To view T C P/I P settings on a Windows 10 computer:
  In Control Panel, open the Network and Sharing Center. Click Change adapter settings
Brief explanation of settings:
  Gateway—Device that nodes use for access to the outside world
  Subnet mask—Used to indicate what portion of an I P address is the network portion (network I D) and what part is the host portion (host I D)
  D N S server—Server responsible for tracking computer names and their I P addresses

## Slide 7: I P Addresses (2 of 2)
You can use the ipconfig utility in a Command Prompt to find out current T C P/I P settings
Two types of I P addresses:
  I P v 4—A 32-bit address
  I P v 6—A 128-bit address

## Slide 8: I P v 4 Addresses (1 of 7)
I P v 4 addresses
  32-bit address organized into four groups of 8 bits each (known as octets)
  Each of the four octets can be any number from 0 to 255
  Some I P addresses are reserved
Example of an I P v 4 address: 72.56.105.12

## Slide 9: I P v 4 Addresses (2 of 7)
Classful addressing
  The dividing line between the network and host portions is determined by the numerical range the IP address falls in
Classful I P v 4 addresses are divided into five classes:
  Class A, Class B, Class C, Class D, and Class E
Classes A, B, and C licensed IP addresses are available for use on the Internet
  Called public IP addresses
A company can use private I P addresses on its private networks
I E E E recommends the following I P addresses be used for private networks:
  10.0.0.0 through 10.255.255.255
  172.16.0.0 through 172.31.255.255
  192.168.0.0 through 192.168.255.255

## Slide 10: I P v 4 Addresses (3 of 7)
Table 3-1 I P address classes
Class | Network octets* | Approximate number of possible networks | Approximate number of IP addresses in each network
A | 1.x.y.z to 126.x.y.z | 126 | 16 million
B | 128.0.x.y to 191.255.x.y | 16,000 | 65,000
C | 192.0.0.x to 223.255.255.x | 2 million | 254

## Slide 11: I P v 4 Addresses (4 of 7)
Classes D and E addresses were not available for general use:
  Class D begin with octets 224–239 and are used for multicasting
  Class E begin with octets 240–254 and are used for research
Table 3-2 Reserved I P addresses
IP address(es) | Function
255.255.255.255 | Used for broadcast messages by TCP/IP background processes. A broadcast message is read by every node on the network.
0.0.0.0 | Currently unassigned
127.0.0.1 through 127.255.255.254 | Used for research or can indicate your own computer, in which case it is called the loopback address.
169.254.0.1 through 169.254.255.254 | Used to create an A P I P A (Automatic Private IP Addressing) address when a computer configured for D H C P first connects to the network and is unable to lease an IPv4 address from the D H C P server.

## Slide 12: I P v 4 Addresses (5 of 7)
Network Address Translation (N A T)—A technique designed to conserve public I P addresses needed by a network
Address translation—Process where a gateway device substitutes the private I P addresses with its own public address
  When these computers need access to other networks or Internet
Port Address Translation (P A T)—Process of assigning a TCP port number to each ongoing session between a local host and Internet host

## Slide 13: I P v 4 Addresses (6 of 7)

## Slide 14: I P v 4 Addresses (7 of 7)
Two variations of N A T to be aware of:
  S N A T (Static (or Source) Network Address Translation)—The gateway assigns the same public IP address to a host each time it makes a request to access the Internet
  D N A T (Dynamic Network Address Translation)—The gateway has a pool of public address that it is free to assign to a local host when it makes a request to access the Internet

## Slide 15: I P v 6 Addresses (1 of 7)
An I P v 6 address has 128 bits written as eight blocks of hexadecimal numbers separated by colons:
  For example, 2001:0000:0B80:0000:0000:00D3:9C5A:00CC
  Each block is 16 bits
  Leading zeros in a four-character hex block can be eliminated
  If blocks contain all zeroes, they can be written as double colons (::), only one set of double colons is used in an I P address
  Therefore, above example can be written two ways:
    2001::B80:0000:0000:D3:9C5A:CC
    2001:0000:B80::D3:9C5A:CC (preferred method because it contains fewest zeroes)

## Slide 16: I P v 6 Addresses (2 of 7)
I P v 6 terminology:
  Link (sometimes called local link)—Any LAN bounded by routers
  An interface is a node’s attachment to a link
  Dual stacked—When a network is configured to use both I P v 4 and I P v 6
    Tunneling—A method used by I P v 6 to transport I P v 6 packets through or over an I P v 4 network
  Interface I D—The last 64 bits or four blocks of an I P v 6 address that identify the interface
  Neighbors—Two or more nodes on the same link

## Slide 17: I P v 6 Addresses (3 of 7)
Types of I P v 6 addresses:
  Unicast address—Specifies a single node on a network
    Global unicast address—Can be routed on the Internet
    Link local unicast address—Can be used for communicating with nodes in the same link
  Multicast address—Packets are delivered to all nodes on a network
  Anycast address—Can identify multiple destinations, with packets delivered to the closest destination

## Slide 18: I P v 6 Addresses (4 of 7)

## Slide 19: I P v 6 Addresses (5 of 7)
Table 3-3 Address prefixes for types of I P v 6 addresses
IP address type | Address prefix | Notes
Global unicast | 2000::/3 | First 3 bits are always 001
Link local unicast | F E 80::/64 | First 64 bits are always 1111 1110 1000 0000 0000 0000 …. 0000
Unique local unicast | FC00::/7 | First 7 bits are always 1111 110
blank | FD00::/8 | First 8 bits are always 1111 1101
Multicast | FF00::/8 | First 8 bits are always 1111 1111

## Slide 20: I P v 6 Addresses (6 of 7)
Auto configuration:
  I P v 6 addressing is designed so that a computer can autoconfigure its own link local I P address
  Similar to how I P v 4 uses an A P I P A address
Step 1—The computer creates its I P v 6 address:
  Uses F E 8 0::/64 as the first 64 bits (called prefix)
  Last 64 bits can be generated in two ways:
    Randomly generated
    Generated from the network adapter’s MAC address
Step 2—The computer checks to make sure its I P address is unique on the network

## Slide 21: I P v 6 Addresses (7 of 7)
Step 3—The computer asks if a router on the network can provide configuration information (message is called a R S or router solicitation)
  If a router responds with D H C P information, the computer uses whatever information this might be (called a R A or router advertisement)
    Such as the I P addresses of D N S server or the network prefix
  Process is called prefix discovery
    The computer uses the prefix to generate its own link local or global I P v 6 address by appending its interface I D to the prefix

## Slide 22: Ports and Sockets (1 of 3)
Port numbers—Ensure data is transmitted to the correct process among multiple processes running on the computer
Socket—Consists of host’s I P address and the port number of an application running on the host:
  Colon separates the two values
  Example—10.43.3.87:23
Port numbers are divided into three types:
  Well-known ports—0 to 1023
  Registered ports—1024 to 49151
  Dynamic and private ports—49152 to 65535

## Slide 23: Ports and Sockets (2 of 3)

## Slide 24: Ports and Sockets (3 of 3)
Protocols not yet covered:
  T F T P (Trivial File Transfer Protocol)
  N T P (Network Time Protocol)
  L D A P (Lightweight Directory Access Protocol)
  S M B (Server Message Block)
  S I P (Session Initiation Protocol)
  H.323

## Slide 25: Domain Names and D N S (Domain Name System) (1 of 3)
Character-based names are easier to remember than numeric I P addresses
Last part of an F Q D N is called the top-level domain (T L D)
Domain names must be registered with an Internet naming authority that works on behalf of I C A N N
  I C A N N restricts what type of hosts can be associated with .arpa, .mil, .int, .edu, and .gov
Name resolution is the process of discovering the I P address of a host when you know the F Q D N

## Slide 26: Domain Names and D N S (Domain Name System) (2 of 3)
Table 3-5 Some well-known top-level domains
Domain suffix | Type of organization
ARPA | Reverse lookup domain (special Internet function)
COM | Commercial
EDU | Educational
GOV | Government
ORG | Noncommercial organization (such as a nonprofit agency)
NET | Network (such as an ISP)
MIL | United States military organization
BIZ | Businesses
INFO | Unrestricted use

## Slide 27: Domain Names and DNS (Domain Name System) (3 of 3)
D N S is an Application layer client-server system of computers and databases made up of these elements:
  namespace—The entire collection of computer names and their associated IP addresses stored in databases on D N S name servers around the globe
  name servers—Hold databases, which are organized in a hierarchical structure
  resolvers—A D N S client that requests information from D N S name servers

## Slide 28: Namespace Databases
Each organization that provides host services is responsible for providing and maintaining its own D N S authoritative servers for public access
  Authoritative server is the authority on computer names and their IP addresses for computers in their domains
The domains that the organization is responsible for managing are called a D N S zone

## Slide 29: Name Servers (1 of 4)
Four common types of D N S servers:
  Primary D N S server—The authoritative name server for the organization
    Holds the authoritative DNS database for the organization’s zones
  Secondary D N S server—Backup authoritative name server for the organization
  Caching D N S server—Accesses the public D N S data and caches the D N S information it collects
  Forwarding D N S server—Receives queries from local clients but doesn’t work to resolve the queries
Any of these server types can co-exist on the same machine

## Slide 30: Name Servers (2 of 4)
D N S name servers are organized in a hierarchical structure
At the root level, 13 clusters of root server hold information used to locate top-level domain (T L D) servers
T L D servers hold information about authoritative servers owned by various organizations

## Slide 31: Name Servers (3 of 4)

## Slide 32: Name Servers (4 of 4)
Ways the resolution process can get more complex:
  Caching server typically is not the same machine as the authoritative server
    Caching server exists only to resolve names for its own local clients
  Name servers within a company might not have access to root servers
  A T L D name server might be aware of an intermediate name server rather than the authoritative name server
Two types of D N S requests:
  Recursive—A query that demands a resolution or the answer “It can’t be found”
  Iterative—A query where the local server issues queries to other servers
    Other servers only provide information if they have it
    Do not demand a resolution

## Slide 33: Resource Records in a D N S Database
Several types of records, called resource records are kept in a D N S database:
  A (Address) record—Stores the name-to-address mapping for a host
  A A A A (Address) record—Holds the name-to-address mapping, the I P address is an I P v 6 type I P address
  C NAME (Canonical Name) record—Holds alternative names for a host
  P T R (Pointer) record—Used for reverse lookups
  N S (Name Server) record—Indicates the authoritative name server for a domain
  M X (Mail Exchanger) record—Identifies a mail server and is used for email traffic
  S R V (Service) record—Identifies the hostname and port of a computer that hosts a specific network services besides email
  T X T (Text) record—Holds any type of free-form text

## Slide 34: D N S Server Software (1 of 2)
BIND (Berkeley Internet Name Domain)—Most popular D N S server software
  Open source—The term for software whose code is publicly available for use and modification
Microsoft D N S Server—Built-in D N S service in the Windows Server O S
For a more secure network:
  Internal and external DNS queries should be handled by different DNS servers
  Can use a firewall to filter or block traffic between networks
D M Z or demilitarized zone
  Area between two firewalls

## Slide 35: D N S Server Software (2 of 2)

## Slide 36: Troubleshooting Address Problems
Event Viewer—One of the first places to start looking for clues when something goes wrong

## Slide 37: Troubleshooting Tools (1 of 12)
Command-link tools are a great resource to troubleshoot network problems
Some of the most helpful tools:
  ping
  i pconfig (Windows only)
  ifconfig (Linux only)
  nslookup
  dig (Linux only)

## Slide 38: Troubleshooting Tools (2 of 12)
ping (Packet Internet Groper)—Used to verify that T C P/I P is:
  Installed
  Bound to the N I C
  Configured correctly
  Communicating with the network
The ping utility sends out a signal called an echo request to another device (request for a response)
  Other computer responds in the form of an echo reply
I C M P (Internet Control Message Protocol)—Protocol used by the echo request/reply to carry error messages and information about the network

## Slide 39: Troubleshooting Tools (3 of 12)
I P v 6 networks use a version of I C M P called I C M P v 6:
  ping6—On Linux computers running IPv6, use ping6 to verify whether an IPv6 host is available
  ping -6—On Windows computers, use ping with the -6 switch to verify connectivity on I P v 6 networks
For the ping6 and ping -6 commands to work over the Internet, you must have access to the I P v 6 Internet

## Slide 40: Troubleshooting Tools (4 of 12)

## Slide 41: Troubleshooting Tools (5 of 12)
ipconfig—Shows current T C P/I P addressing and domain name information on a Windows computer
  Use ipconfig/all to see a more complete summary of T C P/I P addressing information

## Slide 42: Troubleshooting Tools (6 of 12)
ipconfig—Shows current T C P/I P addressing and domain name information on a Windows computer
  Use ipconfig/all to see a more complete summary of T C P/I P addressing information

## Slide 43: Troubleshooting Tools (7 of 12)
ifconfig—Utility to view and manage T C P/I P settings
If your Linux or UNIX system provides a G U I
  Open a shell prompt, then type ifconfig
  Table 3-9 Some ifconfig commands
ifconfig command | Description
ifconfig | Displays basic TCP/IP information and network information, including MAC address of the N I C
ifconfig -a | Displays TCP/IP information associated with every interface on a Linux device; can be used with other parameters (see Figure 3-26)
ifconfig down | Marks the interface, or network connection, as unavailable to the network
ifconfig up | Reinitializes the interface after it has been taken down (via the ifconfig down command), so that it is once again available to the network
man ifconfig | Displays the manual pages, called man pages, for the ifconfig command, which tells you how to use the command and about command parameters (similar to the ipconfig /? command in Windows)

## Slide 44: Troubleshooting Tools (8 of 12)

## Slide 45: Troubleshooting Tools (9 of 12)
n s lookup (name space lookup)—Allows you to query the D N S database from any computer on a network:
  To find the host name of a device by specifying its I P address, or vice versa
  Useful for verifying a host is configured correctly or for troubleshooting D N S resolution problems
Reverse D N S lookup—To find the host name of a device whose I P address you know
  ns lookup 69.23.208.74
Two modes:
  Interactive—To test multiple D N S servers at one time
  Noninteractive—Test a single D N S server

## Slide 46: Troubleshooting Tools (10 of 12)

## Slide 47: Troubleshooting Tools (11 of 12)
You can change D N S servers from within interactive mode with the server subcommand and specifying the IP address of the new D N S server
To exit nslookup’s interactive mode, enter exit

## Slide 48: Troubleshooting Tools (12 of 12)
dig (domain information groper)—Available on Linux and macO S
  Provides more detailed information than nslookup and uses more reliable sources of information to output its results
  Table 3-10 Sample dig commands
Sample dig commands | Description
dig google.com | Performs a D N S lookup on a domain name
dig @8.8.8.8 google.com | Specifies a name server in the google.com domain
dig @8.8.8.8 google.com MX | Requests a list of all A records in the google.com domain on a specific name server
dig google.com ANY | Requests a list of all record types in the google.com domain
dig –x 74.125.21.102 | Performs a reverse lookup on a Google I P address
man dig | Displays the man page for the dig command

## Slide 49: Common Network Issues (1 of 3)
Incorrect time
  Check a domain computer’s time source from a Command Prompt window by entering w32tm /query /source

## Slide 50: Common Network Issues (2 of 3)
D H C P issues:
  If you are getting D H C P errors or if multiple clients are having trouble connecting to the network
    Check the settings on your D H C P server
    Make sure the D H C P scope is large enough to account for the number of clients the network must support
  Consider implementing a shorter lease time on larger networks

## Slide 51: Common Network Issues (3 of 3)
Network connection configuration issues
  Common configuration errors:
    Incorrect netmask
    Incorrect gateway
    Duplicate IP address
  When a computer is struggling to establish a network connection
    Check its T C P/I P configuration settings
  If the computer is not obtaining an I P address and related information from a D H C P server
    Static settings might be using the wrong information
    Try switching to D H C P

## Slide 52: Chapter Summary (1 of 3)
The I A N A is an organization responsible for tracking the assignments of domain names, port numbers, and IP addresses
MAC addresses contain two parts, are 48 bits long, and are written in hexadecimal numbers separated by colons
I P addresses identify nodes at the Network layer
The first part of an I P v 4 address identifies the network and the last part identifies the host
A D H C P scope is a range of addresses to be assigned to clients when they request an I P v 4 address
A gateway device that stands between a private network and other networks substitutes the private I P address with its own public address when computers need access to other networks or the Internet

## Slide 53: Chapter Summary (2 of 3)
I P v 6 standards were developed to improve routing capabilities and speed communication over the established I P v 4 standards
I P v 6 addressing is designed so that a computer can autoconfigure its own link local I P address
A port number is a number, assigned to a process:
  T C P and U D P ports ensure that data is transmitted to the correct process among multiple process running on the computer
Name resolution is the process of discovering the IP address of a host when its F Q D N is known
Namespace databases are stored in D N S zone files
The most popular D N S server software is BIND

## Slide 54: Chapter Summary (3 of 3)
Troubleshooting utilities and tools:
  Event Viewer, ping, ipconfig, ifconfig (Linux only), nslookup, and dig (Linux only)
If your computer is not a member of a domain, you can determine and adjust the time server your computer syncs to when it connects to the Internet
Make sure the D H C P scope is large enough to account for the number of clients the network must support
If the computer is not obtaining an I P address and related information from a D H C P server:
  Static settings might be using the wrong information
  Try switching to D H C P