## Slide 1: Network+ Guide to Networks Eighth Edition
Chapter 5
Network Cabling
© 2019 Cengage. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Objectives
5.1 Explain basic data transmission concepts, including throughput, bandwidth, multiplexing, and common transmission flaws
5.2 Identify and describe the physical characteristics and official standards of coaxial cable, twisted-pair, and fiber-optic cable, and their related connectors
5.3 Compare the benefits and limitations of various networking media
5.4 Select and use the appropriate tool to troubleshoot common cable problems

## Slide 3: Transmission Basics
Transmission techniques in use on today’s network are complex and varied
This section covers:
  Measurements that indicate network efficiency
  Obstacles to good network performance

## Slide 4: Throughput and Bandwidth (1 of 2)
Bandwidth
  The amount of data that could be theoretically transmitted during a given period of time
Throughput
  Measure of how much data is actually transmitted during given time period
Both are commonly expressed as bits transmitted per second, called bit rate

## Slide 5: Throughput and Bandwidth (2 of 2)
Table 5-1 Throughput and bandwidth measures
Quantity | Prefix | Abbreviation
1 bit per second | n/a | 1 bps = 1 bit per second
1000 bits per second | kilo | 1 Kbps = 1 kilobit per second
1,000,000 bits per second | mega | 1Mbps = 1 megabit per second
1,000,000,000 bits per second | giga | 1 Gbps = 1 gigabit per second
1,000,000,000,000 bits per second | tera | 1 Tbps = 1 terabit per second

## Slide 6: Transmission Flaws (1 of 4)
Noise:
  Any undesirable influence degrading or distorting signal
  Measured in d B (decibels)
Types of noise
  E M I (electromagnetic interference):
    Caused by motors, power lines, televisions, copiers, fluorescent lights, etc.
    One type of E M I is R F I (radio frequency interference)
  Cross-talk:
    Signal on one wire infringes on adjacent wire signal
    Alien cross-talk occurs between two cables
    Near end cross-talk (NEXT) occurs near source
    Far end cross-talk (FEXT) occurs at the far end

## Slide 7: Transmission Flaws (2 of 4)

## Slide 8: Transmission Flaws (3 of 4)
Attenuation
  Loss of signal’s strength as it travels away from source
Signals can be boosted:
  Repeater—Regenerates a digital signal in its original form
    Without noise previously accumulated

## Slide 9: Transmission Flaws (4 of 4)
Latency:
  Delay between signal transmission and receipt
  May cause network transmission errors
Latency causes:
  Cable length
  Intervening connectivity device
Round trip time (R T T):
  Time for packet to go from sender to receiver, then back from receiver to sender
If packets experience varying amounts of delay:
  They can arrive out of order
  A problem commonly called jitter or P D V (packet delay variation)

## Slide 10: Duplex, Half-Duplex, and Simplex (1 of 2)
N I C settings include the direction in which signals travel over the media and the number of signals that can traverse the media at any given time
  These two settings are combined to create different methods of communication
Full-duplex—Also called duplex
  Signals travel in both directions over a medium simultaneously
Half-duplex
  Signals may travel in both directions but only in one direction at a time
Simplex
  Signals may travel in only one direction and is sometimes called one-way or unidirectional, communication

## Slide 11: Duplex, Half-Duplex, and Simplex (2 of 2)

## Slide 12: Multiplexing (1 of 4)
Multiplexing
  A form of transmission that allows multiple signals to travel simultaneously over one medium
Subchannels
  Logical multiple smaller channels
Multiplexer (mux):
  Combines many channel signals
  Required at the transmitting end of the channel
Demultiplexer (demux)
  Separates the combined signals

## Slide 13: Multiplexing (2 of 4)
Three types of multiplexing are used on copper lines
T D M (time division multiplexing)
  Divides channel into multiple time intervals
S T D M (statistical time division multiplexing):
  Transmitter assigns slots to nodes
    According to priority and need
  Maximizes available bandwidth on a network
F D M (frequency division multiplexing)
  Assigns different frequency band for each communications subchannel

## Slide 14: Multiplexing (3 of 4)
Three types of multiplexing are used on fiber-optic cable
W D M (wavelength division multiplexing)
  Carries multiple light signals simultaneously by dividing a light beam into different wavelengths or colors
D W D M (dense wavelength division multiplexing):
  Extraordinary capacity
  Typically used on high-bandwidth or long-distance WAN links
C W D M (Coarse wavelength division multiplexing):
  Channels are spaced more widely apart across entire frequency band
  Effective distance is more limited because the signal is not amplified

## Slide 15: Multiplexing (4 of 4)

## Slide 16: Copper Cable
Coaxial cable is considered a “legacy” cable

## Slide 17: Twisted-Pair Cable (1 of 3)
Color-coded insulated copper wire pairs:
  0.4–0.8 mm diameter
  Encased in a plastic sheath
  Every two wires are twisted together

## Slide 18: Twisted-Pair Cable (2 of 3)
Twisted-pair cabling in Ethernet networks contains four wire pairs:
  Fast Ethernet uses one pair to send data and one pair to receive data
  Networks using Gigabit Ethernet use all four pairs for both sending and receiving
Wiring standard specification
  T I A/E I A 568
Most common twisted pair types:
  Category (cat) 3, 5, 5e, 6, 6a, and 7
  CAT 5e or higher used in modern LANs
Two categories:
  Shielded twisted pair (S T P)
  Unshielded twisted pair (U T P)

## Slide 19: Twisted-Pair Cable (3 of 3)

## Slide 20: S T P (Shielded Twisted Pair)
Individually insulated
Surrounded by metallic substance shielding (foil):
  Barrier to external electromagnetic forces
  Contains electrical energy of signals inside
  Must be grounded

## Slide 21: U T P (Unshielded Twisted Pair)
One or more insulated wire pairs encased in plastic sheath:
  No additional shielding
  Less expensive, less noise resistance

## Slide 22: Comparing S T P and U T P
Throughput
  S T P and U T P can transmit the same rates
Cost
  S T P and U T P vary in cost
  S T P is more expensive than U T P
Connector
  S T P and U T P use Registered Jack 45
Noise immunity
  S T P is more noise resistant
Size and scalability
  Maximum segment length for both: 100 meters on Ethernet networks that support data rates from 1 Mbps and 10 Gbps

## Slide 23: Cable Pinouts (1 of 4)
Proper cable termination is a requirement for two nodes on a network to communicate
  Poor terminations can lead to loss or noise in a signal
T I A/E I A specifies two methods of inserting wires into RJ-45 plugs:
  T I A/E I A 568A
  T I A/E I A 568B
No functional difference between the two standards
  Just make sure you use the same standard on every RJ-45 plug and jack

## Slide 24: Cable Pinouts (2 of 4)

## Slide 25: Cable Pinouts (3 of 4)
Straight-through cable (also called patch cable)
  Terminate RJ-45 plugs at both ends identically
Crossover cable
  Transmit and receive wires on one end reversed
Rollover cable (also called console cable):
  All wires are reversed
  Terminations are a mirror image of each other
  Used to connect a computer to the console port of a router
    When making configuration changes to the device

## Slide 26: Cable Pinouts (4 of 4)

## Slide 27: P o E (Power over Ethernet) (1 of 4)
P o E—I E E E 802.3af standard which specifies a method for supplying electrical power over twisted-pair Ethernet connections
Amount of power provided:
  15.4 watts for standard Po E devices
  25.5 watts for newer P o E+ devices (802.3at standard)
P o E standard specifies two types of devices:
  P S E (power sourcing equipment)
  P D (powered devices)

## Slide 28: P o E (Power over Ethernet) (2 of 4)
P o E requires Cat 5 or better copper cable
The I E E E standard requires that a P S E device first determine whether a node is P o E-capable before attempting to supply it with power
On networks that demand P o E but don’t have P o E-capable equipment, you can add P o E adapters

## Slide 29: P o E (Power over Ethernet) (3 of 4)

## Slide 30: P o E (Power over Ethernet) (4 of 4)

## Slide 31: Ethernet Standards for Twisted-Pair Cable (1 of 2)
A cable’s category (Cat 5e or Cat 6) determines the fastest network speed it can support
  A Layer 1 characteristic
A device’s N I C is also rated for maximum network speeds
Most LANs today use devices and N I Cs that can support Fast Ethernet and Gigabit Ethernet
  Devices can auto-negotiate for the fastest standard they have in common

## Slide 32: Ethernet Standards for Twisted-Pair Cable (2 of 2)
Table 5-4 Ethernet standards used with twisted-pair cabling
Standard | Maximum transmission speed (Mbps) | Maximum distance per segment (m) | Physical media | Pairs of wires used for transmission
100Base-T Fast Ethernet | 100 | 100 | Cat 5 or better | 2 pair
1000Base-T Gigabit Ethernet | 1000 | 100 | Cat 5 or better (Cat 5e is preferred) | 4 pair
10GBase-T 10-Gigabit Ethernet | 10,000 | 100 | Cat 6a or Cat 7 (Cat 7 is preferred) | 4 pair

## Slide 33: Fiber-Optic Cable (1 of 4)
Fiber-optic cable (fiber)
  Contains one or more glass or plastic fibers at its center (core)
Data transmission
  Pulsing light sent from laser or light-emitting diode (L E D) through central fibers
Cladding:
  Layer of glass or plastic surrounding fibers
  Different density from glass or plastic in strands
  Reflects light back to core
  Allows fiber to bend

## Slide 34: Fiber-Optic Cable (2 of 4)
Plastic buffer outside cladding:
  Protects cladding and core
  Opaque to absorb escaping light
  Surrounded by Kevlar (polymeric fiber) strands
Plastic sheath covers Kevlar strands

## Slide 35: Fiber-Optic Cable (3 of 4)
Benefits over copper cabling:
  Extremely high throughput
  Very high noise resistance
  Excellent security
  Able to carry signals for longer distances
Drawbacks:
  More expensive than twisted pair cable
  Requires special equipment to splice

## Slide 36: Fiber-Optic Cable (4 of 4)
Throughput
  Proven reliable in transmitting data at rates that can reach 100 gigabits per second per channel
Cost
  Most expensive transmission medium
Noise immunity
  Unaffected by E M I
Size and scalability:
  Segment lengths vary from 2 to 40,000 meters
  Depends on the light’s wavelength and type of cable

## Slide 37: S M F (Single Mode Fiber) (1 of 2)
Consists of narrow core (8–10 microns in diameter):
  Laser-generated light travels over one path
    Little reflection
  Light does not disperse as signal travels
Can carry signals many miles:
  Before repeating is required
Rarely used for shorter connections:
  Due to cost
  The Internet backbone depends on S M F

## Slide 38: S M F (Single Mode Fiber) (2 of 2)

## Slide 39: M M F (Multimode Fiber) (1 of 2)
Contains a core with a larger diameter than single mode fiber
  Common sizes: 50 or 62.5 microns
Laser or L E D generated light pulses travel at different angles
Greater attenuation than single-mode fiber
Common uses:
  Cables connecting routers, switches, and servers on the backbone of a network
  Cables to connect a desktop workstation to the network
Transition between S M F and M M F might occur at an F D P (fiber distribution panel)

## Slide 40: M M F (Multimode Fiber) (2 of 2)

## Slide 41: Fiber Connectors (1 of 3)
M M F connectors
  Classified by the number of fibers
S M F connectors
  Classified by size and shape of the ferrule
Ferrule—The extended tip of a connector that makes contact with the receptacle in the jack

## Slide 42: Fiber Connectors (2 of 3)
Shapes and polishes used by S M F ferrules to reduce back reflection:
  Ultra Polished Connector (U P C)
  Angle Polished Connector (A P C)

## Slide 43: Fiber Connectors (3 of 3)
S M F connectors are typically available with a 1.25-mm ferrule or a 2.5-mm ferrule:
  Most common 1.25-mm connector is the L C (local connector)
  Two 2.5-mm connectors are the S C (standard connector) and ST (straight tip)
Most common M M F connector is the M T R J
Existing fiber networks might use S T or S C connectors
  L C and M T-R J are used on the very latest fiber-optic technology

## Slide 44: Media Converters
Media converter:
  Hardware that enables networks or segments running on different media to interconnect and exchange signals
  Completes the physical connection and converts electrical signals from copper cable to light wave signals
    Can also be used to convert networks using M M F with networks using S M F

## Slide 45: Fiber Transceivers (1 of 4)
Some switches allow you to change and upgrade its interfaces
  They contain sockets where one of many types of modular interfaces, called transceivers, can be plugged in
G B I C—A standard type of modular interface designed for Gigabit Ethernet connections
  May contain RJ-45 or fiber-optic cable ports

## Slide 46: Fiber Transceivers (2 of 4)
Newer transceivers that have made the G B I C obsolete:
  S F P (small form-factor pluggable)
  X F P (10 Gigabit small form-factor pluggable)
  S F P+
  Q S F P (quad small form-factor pluggable)
  Q S F P+
  C F P (centum form-factor pluggable)
To avoid a transceiver mismatch
  Devices must be paired based on supported speeds and protocols

## Slide 47: Fiber Transceivers (3 of 4)

## Slide 48: Fiber Transceivers (4 of 4)
BiDi transceivers:
  Allows bidirectional transmission on both ports
  Means fiber cable carries data in both directions
Installing a transceiver:
  Slide the transceiver into a socket on the back of the connectivity device
  Most S F Ps come with a tab or latch system and keyed so that they will slide into the socket when aligned properly

## Slide 49: Ethernet Standards for Fiber-Optic Cable (1 of 2)
Table 5-6 Ethernet standards using fiber-optic cable
Standard | blank | Maximum transmission speed (Mbps) | Maximum distance per segment (m) | Physical media
Gigabit Ethernet | 1000Base-LX | 1000 | 550 for M M F, 5000 for S M F | M M F or S M F
blank | 1000Base-SX | 1000 | Up to 550, depending on modal bandwidth and fiber core diameter | M M F
10-Gigabit Ethernet | 10GBase-SR and 10GBase-LW | 10,000 | Up to 300, depending on modal bandwidth and fiber core diameter | M M F
blank | 10GBase-LR and 10GBase-LW | 10,000 | 10,000 | S M F
blank | 10GBase-ER and 10GBase-EW | 10,000 | 40,000 | S M F

## Slide 50: Ethernet Standards for Fiber-Optic Cable (2 of 2)
Table 5-7 1000Base-SX Segment lengths
Multimode fiber diameter | Maximum segment length
50 microns | 550 m
62.5 microns | 275 m

## Slide 51: Common Fiber Cable Problems
Fiber type mismatch:
  More of a fiber core mismatch
  Even same-mode cables can be mismatched if the cores have different widths
Wavelength mismatch
  S M F, M M F, and P O F (Plastic Optical Fiber) use different wavelengths
Dirty connectors
  Signal loss and other errors can start to cause problems

## Slide 52: Troubleshooting Tools
Start troubleshooting a network connection problem by checking the network connection L E D status indicator lights:
  Steady light indicates connectivity
  Blinking light indicates activity
  Red or amber light might indicate a problem
If a cabling issue is suspected
  Know which tools are designed to analyze and isolate problems

## Slide 53: Toner and Probe Kit (1 of 3)
Tone generator (toner):
  Small electronic device
  Issues signal on wire pair
Tone locator (probe)
  Emits tone when electrical activity detected
Probe kit or toner probe
  Generator and locator combination
Testing requires trial and error
Used to determine where wired pair terminates
Not used to determine cable characteristics

## Slide 54: Toner and Probe Kit (2 of 3)

## Slide 55: Toner and Probe Kit (3 of 3)

## Slide 56: Multimeter (1 of 2)
Multimeter
  Measures electric circuit characteristics
    Resistance, voltage, and impedance
Use a multimeter to do the following:
  Measure voltage to verify cable is conducting electricity
  Check for the presence of noise
  Test for short or open circuits in the wire:
    Short circuit is an unwanted connection
    Open circuit is one where needed connections are missing

## Slide 57: Multimeter (2 of 2)

## Slide 58: Cable Continuity Tester (1 of 3)
Cable continuity testers (cable testers)
  Tests whether cable carries signal to destination
Copper-based cable tester
  Consists of two parts:
    Base unit generates voltage
    Remote unit detects voltage
Series of lights, audible tone
  Used to signal pass/fail

## Slide 59: Cable Continuity Tester (2 of 3)
Some continuity testers verify U T P, S T P wires paired correctly
  Not shorted, exposed, crossed
Fiber optic continuity tester:
  Issues light pulses on fiber
  Determines whether pulses reach other end
Offer convenience: Portable, lightweight, and low cost

## Slide 60: Cable Continuity Tester (3 of 3)

## Slide 61: Cable Performance Tester (1 of 2)
Cable performance tester, line tester, or certifier
  Performs similarly to continuity testers but can be used to:
    Measure distance to a connectivity device, termination point, or cable fault
    Measure attenuation
    Measure N E X T (near end cross-talk)
    Measure termination resistance and impedance
    Issue pass/fail ratings for Cat 3–7 standards
    Store and print results or save to a computer database
    Graphically depict attenuation and cross-talk

## Slide 62: Cable Performance Tester (2 of 2)
T D R (time domain reflectometer):
  Issue signal, measures signal bounce back
  Indicates distance between nodes
  Indicates whether terminators properly installed, functional
O T D Rs (optical time domain reflectometers):
  Measure fiber length
  Determine faulty splice locations, breaks, connectors, bends, and measure attenuation over cable
  Measure attenuation over the cable
  Can be expensive

## Slide 63: O P M (Optical Power Meter) (1 of 2)
O P M (optical power meter):
  Also called a light meter
  Measures the amount of light power transmitted on a fiber-optic line
  Must be calibrated precisely, following highly accurate optical power standards
  Surrounding room temperature, connection type, and the skill of the technician all affect the final test results

## Slide 64: O P M (Optical Power Meter) (2 of 2)

## Slide 65: Chapter Summary (1 of 4)
Bandwidth is the amount of data that could theoretically be transmitted during a given period of time
Noise can degrade or distort a signal
Duplex signals are free to travel in both directions over a medium simultaneously
Today’s networks might use RG-59 coaxial cable for short connections
Twisted-pair cable consists of color-coded pairs of insulated copper wires that are twisted in pairs:
  S T P cable’s shielding acts as a barrier to external electromagnetic forces
  U T P cable is both less expensive and less resistant to noise than S T P
  S T P and U T P both use RJ-45 modular connectors and data jacks

## Slide 66: Chapter Summary (2 of 4)
A crossover cable has the transmit and receive wires reversed
A router’s console port is used with a console cable, or rollover cable
A crimper pushes on the pins inside an RJ-45 connector so they pierce the wire’s insulation
Data is transmitted through the central fibers of fiber-optic cable via pulsing light sent from a laser or an L E D source
Laser-generated light travels over a single path in S M F cables
M M F contains a core with a larger diameter than S M F over which many pulses of light generated by a laser or L E D light source travel at different angles
Older fiber networks might use ST or SC connectors

## Slide 67: Chapter Summary (3 of 4)
A media converter is hardware that enables networks or segments running on different media to interconnect and exchange signals
Cabling problems unique to fiber include fiber type mismatch, wavelength mismatch, and dirty connectors
Start troubleshooting a network connection problem by checking the network connection L E D status indicator lights
A tone generator issues a signal on a wire that can be detected by a tone locator
A multimeter can measure many characteristics of an electric circuit, including its resistance, voltage, and impedance

## Slide 68: Chapter Summary (4 of 4)
A cable continuity tester is battery operated and has two parts: The base unit that connects to one end of the cable and generates a voltage, and the remote unit that connects to the other end of the cable and detects the voltage
A sophisticated cable performance tester will include T D R (time domain reflector) that issues a signal on a cable and then measures the way the signal bounces back
  Detecting the type and locations of cable defects
An O P M (optical power meter) measures the amount of light power transmitted on a fiber-optic line