## Slide 1: Network+ Guide to Networks Eighth Edition
Chapter 7
Virtualization and Cloud Computing
© 2019 Cengage. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Objectives
7.1 Describe and explain virtualization technologies, including how virtual machines connect with a network and how networking infrastructure devices can be virtualized
7.2 Describe cloud computing categories and models, and discuss concerns regarding cloud connectivity and security
7.3 Secure network connections using encryption protocols
7.4 Configure remote access connections between devices

## Slide 3: Virtualization (1 of 5)
Virtualization
  A virtual, or logical, version of something rather than the actual, or physical, version
Host
  Physical computer “hosting” a virtual machine
Guest
  Each virtual machine
Hypervisor
  Creates and manages a V M
  Manages resource allocation and sharing between a host and any of its guest V Ms

## Slide 4: Virtualization (2 of 5)

## Slide 5: Virtualization (3 of 5)
Two types of hypervisors:
  Type 1—Installs on a computer before any O S and is called a bare-metal hypervisor
  Type 2—Installs in a host O S as an application and is called a hosted hypervisor

## Slide 6: Virtualization (4 of 5)
A V M’s software and hardware characteristics are assigned when it is created in they hypervisor
You can customize the V M with:
  A guest O S
  Amount of memory
  Hard disk size
  Processor type and other options

## Slide 7: Virtualization (5 of 5)

## Slide 8: Network Connection Types (1 of 9)
Every V M has its own v N I C (virtual N I C):
  Can connect the V M to other machines
  Operates at the Data Link layer
Each V M can have several v N I Cs
  Maximum number depends on the limits imposed by the hypervisor
When V M’s v N I C is selected:
  Hypervisor creates a connection between that V M and the host
  Connection might be called a bridge or switch (vSwitch)
One host can support multiple virtual switches
  Controlled by the hypervisor

## Slide 9: Network Connection Types (2 of 9)

## Slide 10: Network Connection Types (3 of 9)
The way a v N I C is configured determines whether the V M is joined to a virtual network or attempts to join the physical LAN the host machine is connected to
Various configurations are called networking modes, the most common are:
  Bridged
  N A T
  Host-only

## Slide 11: Network Connection Types (4 of 9)
Bridged mode:
  v N I C accesses physical network using host machine’s N I C
  Obtains own I P address, default gateway, and netmask from D H C P server on physical LAN
  VM appears to other nodes as just another client or server on the network

## Slide 12: Network Connection Types (5 of 9)

## Slide 13: Network Connection Types (6 of 9)
N A T mode:
  v N I C relies on host machine to act as N A T device
  Obtains I P addressing information from host
  Hypervisor acts as a D H C P server
  Appropriate for V Ms that do not need to be accessed at a known address by other network nodes

## Slide 14: Network Connection Types (7 of 9)

## Slide 15: Network Connection Types (8 of 9)

## Slide 16: Network Connection Types (9 of 9)
Host-only mode:
  V Ms on one host can exchange data with each other and the host
  Cannot communicate with nodes beyond the host
  Never receive or transmit data with host’s physical N I C

## Slide 17: Pros and Cons of Virtualization
Advantages of virtualization:
  Efficient use of resources
  Cost and energy savings
  Fault and threat isolation
  Simple backups, recovery, and replication
Disadvantages:
  Compromised performance
  Increased complexity
  Increased licensing costs
  Single point of failure

## Slide 18: N F V (Network Functions Virtualization) (1 of 2)
Options for virtualizing network devices:
  Virtual firewall—Install a firewall’s O S in a V M on an inexpensive server
  Virtual router—Install a router VM on a server instead of purchasing an expensive hardware router
Advantages of virtualizing network functions:
  Virtual devices can be quickly and sometimes automatically migrated (moved) from one server to another in the event of hardware failure of maintenance
  Resources are utilized more efficiently
  Services can be easily scaled to meet the changing needs of a network

## Slide 19: N F V (Network Functions Virtualization) (2 of 2)
N F V (Network Functions Virtualization):
  Merging physical and virtual network architectures
  Provides flexible, cost-saving options for many types of network devices including:
    Virtual servers
    Data storage
    Load balancers
    Firewall
Keep in mind:
  You will need licenses for each virtualized device
  Interaction between physical and virtual devices introduces a small degree of latency
  Some administrators are not comfortable using a virtual firewall to protect an entire network

## Slide 20: S D N (Software-Defined Networking) (1 of 4)
S D N:
  The virtualization of network services
    An S D N controller (or network controller) manages these services instead of services being directly managed by hardware devices
  S D N controller integrates all of the network’s virtual and physical devices into one cohesive system
  Protocols handle the process of making decisions (called the control plane)
  Physical devices make actual contact with data transmissions as they traverse the network (called the data plane)

## Slide 21: S D N (Software-Defined Networking) (2 of 4)

## Slide 22: S D N (Software-Defined Networking) (3 of 4)

## Slide 23: S D N (Software-Defined Networking) (4 of 4)
Primary advantage to separating the control plane from the data plane
  To provide network technicians with more centralized control of network settings and management
S D N creates the potential to implement more sophisticated network functions while using less-expensive devices
S D N architecture has been expanding to include management of network resources hosted in places other than an organization’s own network

## Slide 24: Cloud Computing (1 of 3)
Internet is frequently pictured as a cloud
Cloud computing
  Flexible provision of data storage, applications, and services to multiple clients over a network
Cloud computing features:
  On-demand service
  Support for multiple platforms
  Resource pooling and consolidation
  Metered service
  Elastic services and storage
    Storage capacity can quickly or automatically be scaled up or down

## Slide 25: Cloud Computing (2 of 3)
Can provide virtual desktops
  Operating environments hosted virtually
Developers can load any kind of software on the servers and test it from afar
  Cloud services provider can make sure the development servers are secure and regularly backed up
Most cloud service providers use virtualization software to supply multiple platforms to multiple users

## Slide 26: Cloud Computing (3 of 3)

## Slide 27: Cloud Computing Categories (1 of 4)
Cloud computing service models are categorized by the types of services provided:
  Traditional
    All hardware, software, and everything else is located and managed at the organization’s location
  I a a S (Infrastructure as a Service)
    Hardware services and network infrastructure devices are provided virtually
    Including end user interfaces such as H V Ds (hosted virtual desktops)
  P a a S (Platform as a Service)
    O S, runtime libraries or modules the OS provides to applications, and the hardware on which the O S runs
  S a a S (Software as a Service)
    Applications

## Slide 28: Cloud Computing Categories (2 of 4)

## Slide 29: Cloud Computing Categories (3 of 4)
X a a S (Anything as a Service or Everything as a Service):
  A broader model
  Cloud can provide any combination of functions

## Slide 30: Cloud Computing Categories (4 of 4)

## Slide 31: Deployment Models
Cloud services are delivered in a variety of deployment models
Public cloud
  Service provided over public transmission lines
Private cloud
  Service established on an organization’s own servers in its own data center
Community cloud
  Service shared between multiple organizations
Hybrid cloud
  Combination of the other service models into a single deployment

## Slide 32: Cloud Connectivity and Security (1 of 2)
Potential risks and limitations:
  I S P’s uptime
  I S P-imposed bandwidth limitations
  Cloud provider’s uptime
  Cloud provider’s backup and security systems
  Misconfiguration that exposes one client’s data to another client
  Unauthorized access to data by cloud provider employees or illegitimate users
  Breaches of confidentiality
  Data security regulations
  Questions over ownership of intellectual property stored in the cloud
  Questions over data maintenance

## Slide 33: Cloud Connectivity and Security (2 of 2)
Potential risks and limitations (continued):
  Risks to the network, proprietary data, or customer information caused by B Y O C (bring your own cloud) services on user’s personal devices
  Reduced consumer confidence, fines, lawsuits, and possibly criminal charges when cloud breaches occur
Way to reduce risks of cloud computing:
  Use encryption
  Carefully choose the method by which your network connects to your cloud resources:
    Internet
    Remote access connections
    Leased line
    Dedicated connection

## Slide 34: Encryption Protocols
Encryption:
  Use of mathematical code, called a cipher, to scramble data into a format that can be read only by reversing the cipher
  Used to keep information private
  Primarily evaluated by three benchmarks:
    Confidentiality
    Integrity
    Availability
The principles above form the standard security model called the C I A triad

## Slide 35: Key Encryption (1 of 3)
Key:
  Random string of characters
  Woven into original data’s bits
  Generates unique data block called ciphertext
  Created according to a specific set of rules (algorithms)
Key encryption can be separated into two categories:
  Private key encryption
  Public key encryption

## Slide 36: Key Encryption (2 of 3)
Private key encryption:
  Data encrypted using single key
    Known only by sender and receiver
  Symmetric encryption
    Same key used during both encryption and decryption
Public key encryption:
  Data encrypted using two keys
  Private key: user knows
  Public key: anyone may request
Public key server:
  Publicly accessible host
  Freely provides users’ public keys

## Slide 37: Key Encryption (3 of 3)
Key pair
  Combination of public and private keys
Asymmetric encryption
  Requires two different keys
Digital certificate
  Holds identification information and the user’s public key
C A (certificate authority)
  Issues, maintains digital certificates
P K I (Public key Infrastructure)
  Use of certificate authorities to associate public keys with certain users

## Slide 38: I P sec (Internet Protocol Security)
I P sec
  Encryption protocol suite that defines rules for encryption, authentication, and key management for T C P/I P transmissions
I P sec creates secure connections in five steps:
  IPsec initiation
  Key management
  Security negotiations
  Data transfer
  Termination
Operates in two modes:
  Transport mode
  Tunnel mode

## Slide 39: S S L (Secure Sockets Layer) and T L S (Transport Layer Security) (1 of 2)
Both are methods of encrypting T C P/I P transmissions
  Including Web pages and data entered into Web forms
Both protocols work side by side and are widely known as S S L/T L S or T L S/S S L
When a client and server establish a S S L/T L S connection, they establish a unique session
  Association between client and server
    Defined by agreement
    Specific set of encryption techniques
  Created by S S L handshake protocol
Handshake protocol
  Allows client and server to authenticate
  Similar to a T C P three-way handshake

## Slide 40: S S L (Secure Sockets Layer) and T L S (Transport Layer Security) (2 of 2)
D T L S (Datagram Transport Layer Security)
  A variant of T L S
  Designed specifically for streaming communications
Applications using D T L S must provide their own means of:
  Packet reordering
  Flow control
  Reliability assurance
D T L S includes security levels that are compatible to T L S
D T L S is commonly used by delay-sensitive applications
  Such as V o I P and tunneling applications

## Slide 41: Remote Access (1 of 4)
Remote access:
  Service that allows a client to connect with and log on to a server, LAN, or WAN in a different geographical location
  Requires a type of R A S (remote access server)
Two types of remote access servers:
  Dedicated devices
  Software running on a server

## Slide 42: Remote Access (2 of 4)

## Slide 43: Remote Access (3 of 4)

## Slide 44: Remote Access (4 of 4)
Types of remote access:
  Point-to-point over a dedicated line
  Terminal emulation, also called remote virtual computing
  Virtual private network (V P N)
Data is often encrypted before it is transmitted over the remote connection:
  Some remote access protocols natively include encryption functionality
  Others must be paired with a specific encryption protocol

## Slide 45: Point-to-Point Remote Access Protocols
An older protocol known as SLIP has been replaced by P P P as the preferred communications protocol for remote access point-to-point connections
P P P (Point-to-Point Protocol)
  A Data Link layer protocol that directly connects two WAN endpoints
P P P can:
  Negotiate and establish a connection between two computers
  Use an authentication protocol to authenticate a client to a remote system
  Support several types of Network layer protocols
  Encrypt the transmissions, although P P P encryption is considered weak by today’s standards

## Slide 46: Terminal Emulation (1 of 7)
Terminal emulation (remote virtual computing)
  Allows a user on one computer to control another computer across a network connection
Examples of command-line software:
  Telnet and S S H
Examples of G U I-based software:
  Remote Desktop for Windows
  join.me
  V N C
  Team Viewer

## Slide 47: Terminal Emulation (2 of 7)
Telnet:
  A terminal emulation utility that allow an administrator or other user to control a computer remotely
  Provides little security for establishing a connection (poor authentication)
  Provides no security for transmitting data (no encryption)
S S H (Secure Shell):
  A collection of protocols that provides for secure authentication and encryption
  Guards against a number of security threats:
    Unauthorized access to a host
    I P spoofing
    Interception of data in transit
    D N S spoofing

## Slide 48: Terminal Emulation (3 of 7)
S S H (continued):
  Developed by S S H Communications Security
    Version requires license fee
  Open source versions available: Open S S H
  Secure connection requires S S H running on both client and server
  Allows for password authentication using public and private key generation
Configuration options:
  Use one of several encryption types
  Require client password
  Perform port forwarding
    Redirect traffic that would normally use an insecure port to a S S H-secured port

## Slide 49: Terminal Emulation (4 of 7)

## Slide 50: Terminal Emulation (5 of 7)
R D P (Remote Desktop Protocol) and V N C (Virtual Network Computing)
  R D P is a Microsoft proprietary protocol used to connect to and control a remote computer
  V N C uses the cross-platform protocol R F B (remote frame buffer) to remotely control a workstation or server
  V N C is open source so many companies have developed their own software that can:
    Run O S es on client computers
    Remotely access computers, tablets, and smartphones
    Remotely control media equipment and surveillance systems

## Slide 51: Terminal Emulation (6 of 7)
Management U R L using H T T P S:
  Networking devices are being configured through a connected computer’s browser that navigates to a management U R L
    User can make changes directly to the device
  Ideally the devices will require encrypted connection over H T T P S
Out-of-band management:
  Relies on a dedicated connection between the network administrator’s computer and each network device
  A remote management card is attached to the network device’s console port
    Or sometimes it is built into the device
  A single device, such as a console server or console router, provides centralized management of all linked devices

## Slide 52: Terminal Emulation (7 of 7)
Remote file access:
  F T P (File Transfer Protocol) is not a form of terminal emulation but it does provide remote file access
  Technologies related to F T P:
    F T P S (F T P Security or F T P Secure)
    S F T P (Secure F T P)
    T F T P (Trivial F T P)

## Slide 53: V P Ns (Virtual Private Networks) (1 of 6)
V P N:
  A network connection encrypted from end to end that creates a private connection to a remote network
  Sometimes referred to as a tunnel
V P Ns can be classified according to three models:
  Site-to-site V P N
  Client-to-site V P N
    Also called host-to-site V P N or remote-access V P N
  Host-to-host V P N

## Slide 54: V P Ns (Virtual Private Networks) (2 of 6)

## Slide 55: V P Ns (Virtual Private Networks) (3 of 6)

## Slide 56: V P Ns (Virtual Private Networks) (4 of 6)
A router-based V P N is the most common implementation on UNIX-based networks
  Server-based V P Ns are most often found on Windows networks
V P N concentrator:
  Authenticates V P N clients
  Establishes tunnels for V P N connections
  Manages encryption for V P N transmissions
Two primary encryption techniques used by V P Ns:
  I P sec
  S S L

## Slide 57: V P Ns (Virtual Private Networks) (5 of 6)

## Slide 58: V P Ns (Virtual Private Networks) (6 of 6)
An enterprise-wide V P N can include elements of both client-to-site and site-to-site models
D M V P N (Dynamic Multipoint V P N)
  A type of enterprise using Cisco devices
  Dynamically creates V P N tunnels between branch locations as needed
    Instead of requiring constant, static tunnels for site-to-site connections

## Slide 59: V P N Tunneling Protocols (1 of 4)
To ensure V P Ns can carry all types of data securely
  Special V P N protocols encapsulate higher-layer protocols in a process known as tunneling
Many V P N tunneling protocols operate at the Data Link layer
  Encapsulate the V P N frame into a Network layer packet
Some V P N tunneling protocols work at Layer 3
  Enables additional features and options
Most tunneling protocols rely on an additional encryption protocol to provide data security

## Slide 60: V P N Tunneling Protocols (2 of 4)

## Slide 61: V P N Tunneling Protocols (3 of 4)
P P T P (Point-to-Point Tunneling Protocol):
  An older Layer 2 protocol that supports encryption, authentication, and access services provided by the V P N server
  Uses T C P segments at the Transport layer
  Outdated and is no longer considered secure
L2 T P (Layer 2 Tunneling Protocol):
  Encapsulates P P P data in a similar manner to P P T P
  Can connect a V P N that uses a mix of equipment types
    It is a standard accepted and used by multiple vendors
  Can connect two routers, a router and a R A S, or a client and a R A S
  Implemented with IPsec for security

## Slide 62: V P N Tunneling Protocols (4 of 4)
G R E (Generic Routing Encapsulation):
  Used to transmit P P P, IP and other kinds of messages through the tunnel
  Used in conjunction with IPsec
Open V P N
  Open-source V P N protocol that uses a custom security protocol called OpenSSL for encryption
I K E v 2:
  A component of the IPsec protocol suite
  Offers fast throughput and good stability when moving between wireless hotspots

## Slide 63: Remote Access Policies (1 of 2)
Common requirements:
  Devices used for remote access must be kept up to date with patches, anti-malware software, and a firewall
  Device access must be controlled by a strong password or biometric measures
  Passwords must be strong and must be changed periodically
  The device’s internal and external storage devices must be encrypted
  Company and customer data that is accessed, transferred, stored, or printed must be kept secure
  The loss or theft of any devices used for remote access must be reported to the company immediately

## Slide 64: Remote Access Policies (2 of 2)
Common requirements (continued):
  Encrypted V P N software must be used to remotely access company network resources
  While remotely connected to the company network, the device must not be connected to the open Internet or any other network not fully owned or controlled by the employee
  Remote sessions must be terminated when not in use

## Slide 65: Chapter Summary (1 of 4)
Virtualization is a virtual, or logical, version of something rather than the actual, or physical, version
V Ms can go through a virtual switch on the host computer to reach the physical network and can communicate with physical or virtual routers, other network devices, and other hosts on the local or another network
A bridged v N I C obtains its own I P address, default gateway, and subnet mask from a D H C P server on the physical LAN
N F V (Network Functions Virtualization) provides flexible, cost-saving options for many types of network devices
S D N (software-defined networking) is a centralized approach to networking that removes most of the decision-making power from network devices

## Slide 66: Chapter Summary (2 of 4)
Cloud computing covers a broad range of services from hosting websites and database servers to providing virtual servers for collaboration or software development
Cloud computing service models are categorized by the type of services they provide
Cloud services are delivered in a variety of deployment models, depending on who manages the cloud and who has access to it
One way to reduce the inherent risks of cloud computing is to use encryption
The most popular kind of encryption encodes the original data’s bits using a key, or a random string of characters to scramble the data and generate a unique and consistently sized data block called ciphertext

## Slide 67: Chapter Summary (3 of 4)
I P sec (Internet Protocol Security) is an encryption protocol suite that defines a set of rules for encryption, authentication, and key management for T C P/IP transmissions
S S L (Secure Sockets Layer) and T L S (Transport Layer Security) are both methods of encrypting T C P/I P transmissions en route between the client and server using public key encryption technology
As a remote user, you can connect to a network and its resources via remote access
P P P (Point-to-Point Protocol) is a Data Link layer protocol that directly connects two WAN endpoints
Terminal emulation allows a user on one computer to control another computer

## Slide 68: Chapter Summary (4 of 4)
S S H (Secure Shell) is a collection of protocols that does both authentication and encryption
R D P (Remote Desktop Protocol) is a Microsoft proprietary protocol used by Windows Remote Desktop and Remote Assistance client/server utilities to connect to and control a remote computer
Three remote file access technologies related to F T P include F T P S, S F T P, and T F T P
A V P N is a network connection encrypted from end to end that creates a private connection to a remote network