## Slide 1: Network+ Guide to Networks Eighth Edition
Chapter 8
Subnets and V LANs
© 2019 Cengage. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Objectives
8.1 Explain the purposes of network segmentation
8.2 Calculate and implement subnets
8.3 Explain how V LANs work and how they’re used

## Slide 3: Network Segmentation (1 of 2)
When a network is segmented into multiple smaller networks:
  Traffic on one network is separated from another network’s traffic
  Each network is its own broadcast domain
Segmentation accomplishes the following:
  Enhance security
  Improve performance
  Simplify troubleshooting

## Slide 4: Network Segmentation (2 of 2)
Networks are commonly segmented according to one of the following groupings:
  Geographic locations
  Departmental boundaries
  Device types

## Slide 5: Subnets (1 of 3)
Example: A business has grown from 20 or 30 computers to having a few hundred computers and devices:
  There is only a single LAN or broadcast domain
  One router serves as the default gateway for the entire network
To better manage network traffic, segment the network so that each floor contains one LAN, or broadcast domain
  Install a router on each floor
You will need to configure clients on each subnet so they know which devices are on their own subnet
  Divide the pool of I P addresses into three groups or subnets (technique called subnetting)

## Slide 6: Subnets (2 of 3)

## Slide 7: Subnets (3 of 3)

## Slide 8: How Subnet Masks Work (1 of 2)
I P v 4 address is divided into two parts:
  Network I D and host I D
Subnet mask is used so devices can determine which part of an I P address is network I D and which part is the host I D:
  Number of 1s in the subnet mask determines the number of bits in the IP address belong to the network I D
  I P address 192.168.123.132 in binary:
  11000000.10101000.01111011.10000100
  Subnet mask 255.255.255.0 in binary:
  11111111.111111111.111111111.00000000
  Network I D: 192.168.123.0
  Host portion: 0.0.0.132

## Slide 9: How Subnet Masks Work (2 of 2)
Table 8-2 Default I P v 4 subnet masks
Network class | Default subnet mask (binary) | Number of bits used for the network information | Default subnet mask (dotted decimal)
A | 11111111 00000000 00000000 00000000 | 8 | 255.0.0.0
B | 11111111 11111111 00000000 00000000 | 16 | 255.255.0.0
C | 11111111 11111111 11111111 00000000 | 24 | 255.255.255.0

## Slide 10: C I D R (Classless Interdomain Routing)
C I D R:
  Provides additional ways of arranging network and host information in an IP address
  Takes the network I D or a host’s IP address and follows it with a forward slash (/), followed by the number of bits used for the network I D
192.168.89.127/24:
  24 represents the number of 1s in the subnet mask and the number of bits in the network I D
  Known as a C I D R block

## Slide 11: I P v 4 Subnet Calculations (1 of 3)
Subnetting:
  Alters the rules of classful I P v 4 addressing
  Called classless addressing
  Borrow bits that would represent host information
  Use those bits instead to represent network information
    Increase the number of bits available for the network I D (increase number of networks)
    Reduce the number of bits available for identifying hosts (decrease number of hosts per network)

## Slide 12: I P v 4 Subnet Calculations (2 of 3)
Table 8-4 Steps to divide IP addresses for network I D 192.168.89.0 into two subnets
Step 1: Borrow from host bits
Network ID | 192 | 168 | 89 | 0
In binary | 11000000 | 10101000 | 01011001 | 00000000
Borrow 1 bit | 11000000 | 10101000 | 01011001 | 00000000
Step 2: Determine the subnet mask
In binary | 11111111 | 11111111 | 11111111 | 10000000
In decimal | 255 | 255 | 255 | 128
Step 3: Determine the network IDs
Network ID 1 | 11000000 | 10101000 | 01011001 | 00000000
In decimal | 192 | 168 | 89 | 0
In C I D R notation | 192.168.89.0/25 | blank | blank | blank
Network ID 2 | 11000000 | 10101000 | 01011001 | 10000000
In decimal | 192 | 168 | 89 | 128
In CIDR notation | 192.168.89.128/25 | blank | blank | blank

## Slide 13: I P v 4 Subnet Calculations (3 of 3)
Table 8-4 (Continued)
Step 4: Determine range of host IP addresses
Subnet 1: | blank | blank | blank | blank
First host, binary | 11000000 | 10101000 | 01011001 | 00000001
First host decimal | 192 | 168 | 89 | 1
Last host, binary | 11000000 | 10101000 | 01011001 | 01111110
Last host, decimal | 192 | 168 | 89 | 126
Subnet 2: | blank | blank | blank | blank
First host, binary | 11000000 | 10101000 | 01011001 | 10000001
First host, decimal | 192 | 168 | 89 | 129
Last host, binary | 11000000 | 10101000 | 01011001 | 11111110
Last host, decimal | 192 | 168 | 89 | 254

## Slide 14: Subnet Mask Tables (1 of 3)
Class A, Class B, and Class C networks can be subnetted:
  Each class has different number of host information bits usable for subnet information
  Varies depending on network class and the way subnetting is used
Table 8-6 (see the next slide)
  Lists the number of subnets and hosts that can be created by subnetting a Class B network
Table 8-7 (see the following slide)
  Lists the numbers of subnets and hosts that can be created by subnetting a Class C network

## Slide 15: Subnet Mask Tables (2 of 3)
Table 8-6 I P v 4 Class B subnet masks
Subnet mask | C I D R notation | Number of subnets on network | Number of hosts per subnet
255.255.128.0 | /17 | 2 | 32,766
255.255.192.0 | /18 | 4 | 16,382
255.255.224.0 | /19 | 8 | 8190
255.255.240.0 | /20 | 16 | 4094
255.255.248 | /21 | 32 | 2046
255.255.252.0 | /22 | 64 | 1022
255.255.254.0 | /23 | 128 | 510
255.255.255.0 | /24 | 256 | 254
255.255.255.128 | /25 | 512 | 126
255.255.255.192 | /26 | 1024 | 62
255.255.255.224 | /27 | 2048 | 30
255.255.255.240 | /28 | 4096 | 14
255.255.255.248 | /29 | 8192 | 6
255.255.255.252 | /30 | 16,384 | 2

## Slide 16: Subnet Mask Tables (3 of 3)
Table 8-7 I P v 4 Class C subnet masks
Subnet mask | C I D R notation | Number of subnets on network | Number of hosts per subnet
255.255.255.128 | /25 | 2 | 126
255.255.255.192 | /26 | 4 | 62
255.255.255.224 | /27 | 8 | 30
255.255.255.240 | /28 | 16 | 14
255.255.255.248 | /29 | 32 | 6
255.255.255.252 | /30 | 64 | 2

## Slide 17: Subnetting Questions on Exams
Likely to see two types of subnet calculation problems:
  Given certain network requirements (required number of hosts or subnets), calculate possible subnets and host I P address ranges
  Given an I P address, determine its subnet’s network I D, broadcast address, and first/last host addresses

## Slide 18: Implement Subnets (1 of 3)
Figure 8-7 shows the subnets assigned to the three LANs earlier in Figure 8-3

## Slide 19: Implement Subnets (2 of 3)
Figure 8-8 illustrates a network subnetted into 6 smaller networks

## Slide 20: Implement Subnets (3 of 3)
A centrally managed D H C P server can provide D H C P assignments to multiple subnets with the help of D H C P relay agent:
  A router, firewall, or Layer 3 switch receives the D H C P request from a client in one of its local broadcast domains
  The Layer 3 device creates a message of its own and routes this transmission to the specified D H C P server in a different broadcast domain
  D H C P server notes the relay agent’s IP address and assigns the D H C P client an I P address on the same subnet

## Slide 21: V L S M (Variable Length Subnet Mask) (1 of 3)
V L S M:
  Allows subnets to be further subdivided into smaller and smaller groupings until each subnet is about the same size as the necessary IP address space
  Often referred to as “subnetting a subnet”
To create V L S M subnets:
  Create the largest subnet first
  Create the next largest subnet, and the next one, and so on

## Slide 22: V L S M (Variable Length Subnet Mask) (2 of 3)
Table 8-8 Subnets of various sizes needed on the network
Subnet | Included hosts | Number of hosts | C I D R notation (as calculated next)
1 | Sales | 120 | 192.168.10.0 /25
2 | Accounting | 58 | 192.168.10.128 /26
3 | H R | 25 | 192.168.10.192 /27
4 | I T | 6 | 192.168.10.224 /29
5 | Executives | 5 | 192.168.10.232 /29
6 | WAN link | 2 | 192.168.10.240 /30
7 | WAN link | 2 | 192.168.10.244 /30

## Slide 23: V L S M (Variable Length Subnet Mask) (3 of 3)

## Slide 24: Subnets in I P v 6 (1 of 3)
Subnetting in I P v 6 is simpler than I P v 4
  Classes not used
  Subnet masks not used
  Single I P v 6 subnet is capable of supplying 18,446,744,073,709,551,616 I P v 6 addresses
Subnetting helps administrators manage the enormous volume of I P v 6 addresses
I P v 6 address commonly written as eight blocks of four hexadecimal characters:
  Last four blocks identify the interface
  First four blocks identify the network and serve as the network prefix (also called the site prefix or global routing prefix)
  Fourth hexadecimal block in the site prefix can be altered to create subnets

## Slide 25: Subnets in I P v 6 (2 of 3)

## Slide 26: Subnets in I P v 6 (3 of 3)

## Slide 27: V L A Ns (Virtual Local Area Networks) (1 of 2)
V L A N (virtual local area network):
  Groups ports on a switch so that some of the local traffic on the switch is forced to go through a router
  Limiting traffic to a smaller broadcast domain

## Slide 28: V L A Ns (Virtual Local Area Networks) (2 of 2)
Reasons for using V L A Ns:
  Isolating connections with heavy or unpredictable traffic patterns
  Identifying groups of devices whose data should be given priority handling
  Containing groups of devices that rely on legacy protocols incompatible with the majority of the network’s traffic
  Separating groups of users who need special security or network functions
  Configuring temporary networks
  Reducing the cost of networking equipment

## Slide 29: Managed Switches (1 of 8)
Unmanaged switch
  Provides plug-and-play simplicity with minimal configuration
    Has no I P address assigned to it
Managed switch:
  Can be configured via a command-line interface or a web-based management G U I
  Are usually assigned an IP address
  V LANS can only be implemented through managed switches
  Ports can be partitioned into groups

## Slide 30: Managed Switches (2 of 8)

## Slide 31: Managed Switches (3 of 8)
Figure 8-18 shows how a normal Layer 2 switch operates

## Slide 32: Managed Switches (4 of 8)
Figure 8-19 shows what happens when ports on a managed switch are partitioned into two V LANs

## Slide 33: Managed Switches (5 of 8)
V LAN ports do not have to be next to each other
  See Figure 8-20

## Slide 34: Managed Switches (6 of 8)
802.1 Q
  The I E E E standard that specifies how V LAN information appears in frames and how switches interpret that information
To identify the transmissions that belong to each V LAN
  The switch adds a tag to Ethernet frames that identifies the port through which they arrive at the switch
Tag travels with transmission until it reaches a router or the switch port connected to the destination device (whichever comes first)
If frame is being routed to a new V LAN:
  Router adds a new tag
  Tag is removed once frame reaches its final switch port

## Slide 35: Managed Switches (7 of 8)

## Slide 36: Managed Switches (8 of 8)

## Slide 37: Switch Ports and Trunks (1 of 3)
A port on a switch is configured as either an access port or a trunk port:
  Access port—Used for connecting a single node
  Trunk port—Capable of managing traffic among multiple V LANs
Trunk
  A single physical connection between switches through which many logical V LANs can transmit and receive data
Trunking protocols assign and interpret V LAN tags in Ethernet frames
Cisco’s V T P (V LAN trunking protocol):
  The most popular protocol for exchanging V LAN information over trunks
  V T P allows changes to V LAN database on one switch, called the stack master, to be communicated to all other switches in the network

## Slide 38: Switch Ports and Trunks (2 of 3)

## Slide 39: Switch Ports and Trunks (3 of 3)

## Slide 40: V LANs and Subnets
Each V LAN is assigned its own subnet of I P addresses
Sample network in Figure 8-22 (See on slide 36) is divided into three subnets
  Router sees three logical, virtual LANs connected to a single router port

## Slide 41: Types of V LANs
V LAN types:
  Default V LAN—Typically preconfigured on a switch and initially includes all switch ports
  Native V LAN—Receives all untagged frames from untagged ports
  Data V LAN—Carries user-generated traffic, such as email, web browsing, or database updates
  Management V LAN—Can be used to provide administrative access to a switch
  Voice V LAN—Supports V o I P traffic

## Slide 42: View Configured V LANs (1 of 2)
Once created maintain V LANs via switch software
Figure 8-27 (See next slide) illustrates the result of a show vlan command on a Cisco switch
  This command is used to list the current V LAN recognized by a switch

## Slide 43: View Configured V LANs (2 of 2)

## Slide 44: Troubleshoot and Secure V LANs (1 of 3)
Common configuration errors:
  Incorrect port mode—Switch ports connected to endpoints should nearly always use access mode
  Incorrect V LAN assignment—Can happen due to a variety of situations
  V LAN isolation—You can potentially cut off an entire group from the rest of the network
V LAN hopping:
    Occurs when an attacker generates transmissions that appear to belong to a protected V LAN
    Crosses V LANs to access sensitive data or inject harmful software

## Slide 45: Troubleshoot and Secure V LANs (2 of 3)
Two approaches to V LAN hopping:
  Double tagging—Hacker stacks V LAN tags in Ethernet frames
    First, legitimate tag is removed by switch
    Second, illegitimate tag is revealed, tricking switch into forwarding transmission on to a restricted V LAN
  Switch spoofing—Attacker connects to a switch and makes the connection look to the switch as if it’s a trunk line
    Hacker can feed his own V LAN traffic into that port and access V LANs throughout the network

## Slide 46: Troubleshoot and Secure V LANs (3 of 3)
Mitigation efforts to reduce the risk of V LAN hopping:
  Don’t use the default V LAN
  Change the native V LAN to an unused V LAN I D
  Disable auto-trunking on switches that don’t need to support traffic from multiple V LANs
  On switches that carry traffic from multiple V LANs, configure all ports as access ports unless they are used as trunk ports
  Specify which V LANs are supported on each trunk instead of accepting a range of all V LANs
  Use physical security methods such as door locks to restrict access to network equipment

## Slide 47: Chapter Summary (1 of 3)
When a network is segmented into multiple smaller networks, traffic on one network is separated from another network’s traffic
Subnetting helps solve the fundamental problem with classful addressing
Computers compare the bits in their own network I D to the bits in the network I D of the destination host
C I D R notation takes the network I D or a host’s IP address and follows it with a forward slash (/) followed by the number of bits used for network I D
To create a subnet, borrow bits that would represent host information in classful addressing

## Slide 48: Chapter Summary (2 of 3)
Class A, Class B, and Class C networks can all be subnetted
Two types of subnet calculation problems likely on Network+ exam: calculate possible subnets or calculate subnet information for a single IP address
In dynamic addressing, administrator programs each subnet’s D H C P server with the network I D, subnet mask, range of IP addresses, and default gateway
V L S M allows subnets to be further subdivided into smaller and smaller groupings until each subnet is about the same size as the I P address space that is needed
Subnetting in IPv6 is simpler than subnetting in I P v 4
A V LAN groups ports on a switch so that some of the local traffic is forced to go through a router creating a smaller broadcast domain

## Slide 49: Chapter Summary (3 of 3)
Managed switches can be configured via a command-line interface or a web-based management G U I
A single switch can support traffic belonging to several V LANs across the network
In most situations, each V LAN is assigned its own subnet of IP addresses
Just as different types of I P addresses serve different purposes, so different types of V LANS
Once you create a V LAN, you also maintain it via the switch’s software
Hackers sometimes take advantage of the way V LANs are tagged to implement an attack called V LAN hopping