## Slide 1: Network+ Guide to Networks Eighth Edition
Chapter 10
Security in Network Design
© 2019 Cengage. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Objectives (1 of 2)
10.1 Describe the functions and features of various network security devices
10.2 Implement security precautions on a switch
10.3 Track the processes of authentication, authorization, and auditing on a network

## Slide 3: Objectives (2 of 2)
10.4 Explain the available options in network access control methods
10.5 Configure various security measures on a wireless network

## Slide 4: Network Security Devices
Non-security devices with security features
  Proxy servers and A C Ls
Specialized security devices
  Firewalls and I D S/I P S systems
Using multiple options for network security results in layered security
  Provides more protection than any one type of device

## Slide 5: Proxy Servers (1 of 2)
Proxy server:
  Acts as an intermediary between external and internal networks
  Screens all incoming and outgoing traffic
  Manages security at Application layer
  Appears as an internal network server to the outside world, but is a filtering device for internal LAN
  One of its most important functions is preventing the outside world from discovering the addresses of the internal network
Reverse proxy:
  Provides services to Internet clients from servers on its own network
  Provides identity protection for the server rather than the client
  Useful when multiple Web servers are accessed through the same public I P address

## Slide 6: Proxy Servers (2 of 2)

## Slide 7: A C Ls (Access Control Lists) on Network Devices (1 of 4)
Router’s main functions:
  Examine packets
  Determine destination based on Network layer addressing information
A C L (access control list):
  Used by routers to decline forwarding certain packets
  Acts like a filter to instruct the router to permit or deny traffic according to one or more of the following variables:
    Network layer protocol (e.g., IP or I C M P)
    Transport layer protocol (e.g., T C P or U D P)
    Source IP address
    Destination IP address
    T C P or U D P port number

## Slide 8: A C Ls (Access Control Lists) on Network Devices (2 of 4)
Router receives packet, examines packet:
  Refers to A C L for permit, deny criteria
  Drops packet if deny characteristics match
  Forwards packet if permit characteristics match
  If the packet does not match any criteria given, the packet is dropped
    Called the implicit deny rule
On most routers, each interface must be assigned a separate A C L
  Different A C Ls may be associated with inbound and outbound traffic

## Slide 9: A C Ls (Access Control Lists) on Network Devices (3 of 4)

## Slide 10: A C Ls (Access Control Lists) on Network Devices (4 of 4)
The access-list command is used to assign a statement to an already-installed A C L
  Must identify the A C L and include a permit or deny argument
Example: To permit I C M P traffic from any IP address or network to any I P address or network:
  access-list acl_2 permit i c m p any
Example: To permit T C P traffic from 2.2.2.2 host machine to 5.5.5.5 host machine:
  access-list acl_2 permit t c p host 2.2.2.2 host 5.5.5.5
A C Ls do affect router performance
  The more statements or tests a router must scan the more time it takes a router to act

## Slide 11: Firewalls (1 of 9)
A firewall is a specialized device or software that selectively filters or blocks traffic between networks
  Typically involves hardware and software combination
Firewall location:
  Between two interconnected private networks
  Between private and public networks (network-based firewall)
  May also see firewall features integrated in routers, switches, and other network devices
Other types of firewalls only protect the computer on which they are installed
  Known as host-based firewalls

## Slide 12: Firewalls (2 of 9)

## Slide 13: Firewalls (3 of 9)

## Slide 14: Firewalls (4 of 9)
Packet-filtering firewall:
  Simplest firewall
  Examines header of every entering packet (inbound traffic)
  Can block traffic entering or exiting a LAN (outbound traffic)
Firewall default configuration:
  Blocks most common security threats
  Preconfigured to accept and deny certain traffic types
  Network administrators often customize settings

## Slide 15: Firewalls (5 of 9)

## Slide 16: Firewalls (6 of 9)
Common packet-filtering firewall criteria:
  Source and destination IP addresses
  Source and destination ports
  Flags set in the T C P header
  Transmissions using U D P or I C M P protocols
  Packet’s status as the first packet in new data stream, subsequent packet
  Packet’s status as inbound to, outbound from private network

## Slide 17: Firewalls (7 of 9)
Port blocking
  Prevents connection to and transmission completion through ports
Optional firewall functions:
  Encryption
  User authentication
  Centralized management
  Easy rule establishment
  Content-filtering based on data contained in packets
  Logging, auditing capabilities
  Protect internal LAN’s address identity
  Monitor packets according to existing traffic streams (stateful firewall)
    A stateless firewall manages each incoming packet as a stand-along entity without regard to active connections

## Slide 18: Firewalls (8 of 9)
Unified Threat Management (U T M):
  Security strategy that combines multiple layers of security appliances and technologies into a single safety net
  Requires a great deal of processing power
Next Generation Firewalls (N G F W):
  Have built-in Application Control features and are application aware
    They can monitor and limit traffic of specific applications
  Adapt to the class of a specific user or user group
  May also be context aware
    They adapt to various applications, users, and devices

## Slide 19: Firewalls (9 of 9)
Troubleshooting firewalls:
  Most common cause of firewall failure is firewall misconfiguration
  Configuration must not be so strict that it prevents authorized users from transmitting and receiving necessary data
    But no so lenient that you unnecessarily risk security breaches
  You may need to create exceptions to the rules
    Referred to as “punching a hole” in the firewall

## Slide 20: I D S (Intrusion Detection System) (1 of 2)
I D S (intrusion detection system):
  Stand-along device, an application, or a built-in feature running on a workstation, server, switch, router, or firewall
  Monitors network traffic and generates alerts about suspicious activity
  Commonly exists as an embedded feature in U T M solutions or N G F Ws
Two primary methods for detecting threats:
  Statistical anomaly detection
    Compares network traffic samples to a predetermined baseline in order to detect anomalies
  Signature-based detection
    Looks for identifiable patterns (signatures) of code that are known to indicate specific vulnerabilities, exploits, or other undesirable traffic

## Slide 21: I D S (Intrusion Detection System) (2 of 2)
I D S implementations:
  H I D S (host-based I D S) runs on a single computer to alert about attacks to that one host
    Might also include F I M (file integrity monitoring) which alerts when any changes made to files that shouldn’t change
  N I D S (network-based I D S) protects a network and is usually situated at the edge of the network or in the D M Z (demilitarized zone)
    Network’s protective perimeter
Port mirroring
  One port makes copy of traffic and sends to second port for monitoring
I D S drawback
  Number of false positives logged

## Slide 22: I P S (Intrusion Prevention System) (1 of 2)
I D S can only detect and log suspicious activity
I P S (intrusion prevention system):
  Reacts to suspicious activity when alerted
  Detects threat and prevents traffic from flowing to network
    Based on originating IP address
N I P S (network-based intrusion prevention)
  Protects entire networks
H I P S (host-based intrusion prevention)
  Protects certain hosts

## Slide 23: I P S (Intrusion Prevention System) (2 of 2)

## Slide 24: S I E M (Security Information and Event Management)
S I E M systems can be configured to evaluate all log data
  Looking for significant events that require attention from the IT staff
Effectiveness of the S I E M
  Determined by the amount of storage space needed for the amount of data generated
Network administrators can fine-tune a S I E M’s configuration rules for the specific needs
  Which event should trigger responses
Network technicians should review raw data on a regular basis
  To ensure no glaring indicators are being missed by existing rules

## Slide 25: Switch Management
This section covers the following:
  How paths between switches are managed
  Switch security concerns (Physical, Data Link, and Network layers)

## Slide 26: Switch Path Management (1 of 5)
To make networks more fault tolerant
  You install multiple (redundant) switches at critical junctures
Redundancy allows data the option of traveling through more than one switch
  Makes a network less vulnerable to hardware malfunctions
A potential problem with redundant paths is traffic loops

## Slide 27: Switch Path Management (2 of 5)
S T P (Spanning Tree Protocol):
  Defined in I E E E standard 802.1D
  Operates in Data Link layer
S T P prevents traffic loops:
  Calculating paths avoiding potential loops
  Artificially blocking links completing loop
If a switch is removed, S T P will recalculate the best loop-free data paths between the remaining switches

## Slide 28: Switch Path Management (3 of 5)
Three steps:
  Select root bridge based on Bridge I D (B I D)
  Examine possible paths between network bridge and root bridge
  Disables links not part of shortest path

## Slide 29: Switch Path Management (4 of 5)
S T P information is transmitted between switches
  Via B P D Us (Bridge Protocol Data Units)
Security precautions that must be configured on S T P-enabled interfaces:
  B P D U guard—Blocks B P D Us on any port serving network hosts
    Ensures these devices aren’t considered as possible paths
  B P D U filter—Can be used to disable S T P on specific ports
  Root guard—Prevents switches beyond the configured port from becoming the root bridge

## Slide 30: Switch Path Management (5 of 5)
Newer (faster) versions of S T P include:
R S T P (Rapid Spanning Tree Protocol) and M S T P (Multiple Spanning Tree Protocol)
T R I L L (Transparent Interconnection of Lots of Links)
  A multipath, link-state protocol
S P B (Shortest Path Bridging)
  A descendent of S T P that operates at Layer 3
  Keeps all potential paths active while managing flow of data
Some switch manufacturers have designed proprietary versions of S T P
  Example: Cisco and Extreme Networks

## Slide 31: Switch Port Security
Unused physical and virtual ports on switches and other network devices should be disabled:
  Use the shutdown command on Cisco, Huawei, and Arista routers and switches
  Use the no shutdown command to enable them again
Another Cisco command (also used on Arista devices) to secure switch access ports:
  Switchport port-security (or just port-security on Huawei switches)
  Essentially a MAC filtering functions that also protects against MAC flooding
On a Juniper switch:
  The mac-limit command restricts the number of MAC addresses allowed in the MAC address table
  Allowed MAC addresses are configured with the allowed-mac command

## Slide 32: A A A (Authentication, Authorization, and Accounting)
Controlling users’ access to a network and its resources consists of three major elements:
  Authentication—Process of verifying user’s credentials to grant user access to secured resources
  Authorization—Determines what the user can and cannot do with network resources
  Accounting—To keep an account of the client’s system or network usage

## Slide 33: Authentication (1 of 3)
A user can be authenticated to the local device or to the network
Local authentication—Usernames and passwords are stored locally which has both advantages and disadvantages:
  Low security
  Convenience varies
  Reliable backup access
With local authentication
  Every computer on the network is responsible for securing its own resources
In Windows
  Switch from local authentication to network authentication on the domain using the System Properties dialog box

## Slide 34: Authentication (2 of 3)

## Slide 35: Authentication (3 of 3)
Network authentication and logon restrictions:
  Harden your network by requiring secure passwords to authenticate to the network
  Additional authentication restrictions that strengthen network security:
    Time of day
    Total time logged on
    Source address
    Unsuccessful logon attempts
    Geographic location (geofencing)

## Slide 36: Authorization (1 of 2)
User access to network resources falls into one of the two categories:
  The privilege or right to execute, install, and uninstall software
  Permission to read, modify, create, or delete files and folders
R B A C (role-based access control):
  Most popular authorization method
  Administrator assigns privileges and permissions necessary for users to perform their roles (duties)
  Administrators create groups associated with certain roles
Role separation
  Each user can only be a member of a single group

## Slide 37: Authorization (2 of 2)

## Slide 38: Accounting
A log file viewer can be installed to make it easier to monitor log files for interesting or suspicious events
In Windows, use Event viewer to view Windows logs

## Slide 39: N A C (Network Access Control) (1 of 2)
A network access control (N A C) solution employs a set of rules called network policies which determine the level and type of access granted to a device when it joins a network
N A C authenticates and authorizes devices
  By verifying that the device complies with predefined security benchmarks
An agent can be installed on the device before it can be authenticated
  Monitors device’s status to determine the device’s compliance

## Slide 40: N A C (Network Access Control) (2 of 2)
Two types of agents:
  Nonpersistent agent remains on the device long enough to verify compliance and complete authentication and then uninstalls
    Also called dissolvable agent
  Persistent agent is permanently installed on a device
Devices that do not meet compliance requirements can be placed in a quarantine network
  Separate from sensitive network resources

## Slide 41: Access Control Technologies
Authentication protocols
  The rules computers follow to accomplish authentication
Several types of authentication services and protocols exist

## Slide 42: Directory Services
Directory service
  Maintains a database of account information, such as, usernames, passwords, and other authentication credentials
Examples:
  A D (Active Directory) in Windows
  Open L D A P
  389 Directory Server
L D A P (Lightweight Directory Access Protocol):
  Standard protocol for accessing an existing directory
  All the above are built to be L D A P-compliant
AD is configured to use the Kerberos protocol

## Slide 43: Kerberos (1 of 6)
Kerberos
  Cross-platform authentication protocol
Uses key encryption:
  Verifies client identity
  Securely exchanges information after client logs on
Example of a private key encryption service
Provides significant security advantages over simple N O S authentication

## Slide 44: Kerberos (2 of 6)
Terms:
  Principal
  K D C (Key Distribution Center)
  Ticket
  Kerberos server runs two services:
  A S (authentication service)
    Initially validates a client
  T G S (ticket-granting service)
    An application running separate from the AS that also runs on the K D C
    Alleviates the need for the client to request a new ticket from the T G S each time it wants to use a different service on the network

## Slide 45: Kerberos (3 of 6)

## Slide 46: Kerberos (4 of 6)

## Slide 47: Kerberos (5 of 6)

## Slide 48: Kerberos (6 of 6)

## Slide 49: S S O (Single Sign-On) (1 of 2)
S S O:
  Form of authentication in which a client signs on one time to access multiple systems or resources
  Primary advantage is convenience
  Disadvantage is that once authentication is cleared, the user has access to numerous resources
2F A (two-factor authentication)
  User must provide something and know something
M F A (multifactor authentication)
  Process that requires two or more pieces of information

## Slide 50: S S O (Single Sign-On) (2 of 2)
Five categories of authentication factors:
  Something you know—password or PIN
  Something you have—A T M or smart card
  Something you are—fingerprint or facial pattern
  Somewhere you are—location in a specific building
  Something you do—specific way you type or speak
M F A requires at least one authentication method from at least two different categories
Security token
  A device or application that stores or generates information

## Slide 51: RADIUS (Remote Authentication Dial-In User Service) (1 of 2)
RADIUS (Remote Authentication Dial-In User Service):
  Open-source and standardized by the I E T F
  Runs in the Application layer and can use either U D P or T C P in the Transport layer
  Can operate as application on remote access server
    Or on dedicated RADIUS server
  Highly scalable
  May be used to authenticate wireless, mobile, and remote users
  RADIUS services are often combined with other network services on a single machine

## Slide 52: RADIUS (Remote Authentication Dial-In User Service) (2 of 2)

## Slide 53: T A C A C S+ (Terminal Access Controller Access Control System Plus)
T A C A C S+ (Terminal Access Controller Access Control System Plus):
  Offers the option of separating authentication, authorization, and auditing capabilities
  Differences from RADIUS:
    Relies on T C P, not U D P, at the Transport layer
    Proprietary protocol developed by Cisco Systems, Inc.
    Typically installed on a router or switch, rather than a server
    Encrypts all information transmitted for AAA

## Slide 54: Wireless Network Security
Recall a disadvantage of W E P
  Used a shared key for all clients and the key might never change
W E P offered two forms of authentication:
  O S A (Open System Authentication)
  S K A (Shared Key Authentication)

## Slide 55: W P A (Wi-Fi Protected Access)
T K I P (Temporal Key Integrity Protocol)
  Encryption key generation and management scheme
T K I P accomplishments:
  Message integrity
  Key distribution
  Encryption
T K I P was a quick fix and is only offered today in order to provide compatibility with older wireless devices

## Slide 56: W P A2 (Wi-Fi Protected Access, version 2)
Data confidentiality methods used in W P A were replaced by stronger technologies
C C M P—Short for Counter Mode with C B C (Cipher Block Chaining) MAC (Message Authentication Code) Protocol
  Improves wireless security for newer devices that can use W P A2
C C M P helps ensure data confidentiality with both encryption and packet authentication by providing:
  Message integrity
  Encryption—Uses A E S (Advanced Encryption Standard), which provides faster and more secure encryption than T K I P

## Slide 57: Personal and Enterprise (1 of 6)
Personal versions of W P A and W P A2:
  Sometimes referred to as W P A-P S K or W P A2-P S K
  P S K is short for Pre-Shared Key
Enterprise versions of W P A and W P A2:
  Implement additional security measures
  A RADIUS server is used in cooperation with an authentication mechanism called E A P (Extensible Authentication Protocol)

## Slide 58: Personal and Enterprise (2 of 6)
Three main E A P entities (shown in Figure 10-29 on previous slide):
  Supplicant—Device requesting authentication
  Authenticator—Device that initiates the authentication process (wireless access point)
  Authentication server—Server that performs authentication

## Slide 59: Personal and Enterprise (3 of 6)

## Slide 60: Personal and Enterprise (4 of 6)
E A P-T L S
  Uses T L S encryption to protect communications
  Uses P K I certificates to exchange public keys and authenticate both supplicant and the server (called mutual authentication)

## Slide 61: Personal and Enterprise (5 of 6)
P E A P (Protected E A P)
  Tunnel-based
  Creates an encrypted T L S tunnel between the supplicant and the server

## Slide 62: Personal and Enterprise (6 of 6)
E A P-F A S T (E A P-Flexible Authentication via Secure Tunneling)
  A form of tunneled E A P
  Developed by Cisco and works similarly to PEAP (only faster)
  Uses P A Cs (Protected Access Credentials) stored on the supplicant device for speedier establishment of the T L S tunnel

## Slide 63: Chapter Summary (1 of 4)
A proxy server acts as an intermediary between the external and internal networks
Thanks to a router’s A C L or access list, routers can decline to forward certain packets depending on their content
A firewall is a specialized device or software that selectively filters or blocks traffic between networks
An I D S (intrusion detection system) is a stand-alone device, an application, or a built-in feature running on a workstation, server, switch, router, or firewall, which is used to monitor network traffic
I D S, I P S, firewalls, and proxy servers all generate a great deal of data that is stored in logs and must be monitored and analyzed

## Slide 64: Chapter Summary (2 of 4)
S T P (Spanning Tree Protocol) prevents traffic loops by calculating paths that avoid potential loops and blocking links that would complete a loop
Unused physical and virtual ports on switches and other network devices should be disabled until needed
Controlling users’ access to a network consists of three major elements: authentication, authorization, and accounting
With geofencing, G P S or R F I D data is sent to the authentication server to report the location of the device attempting to authenticate to the network
Systems generate many logs that can be used for troubleshooting and auditing
A N A C system employs a set of rules, called network policies, which determine the level and type of access granted to a device when it joins a network

## Slide 65: Chapter Summary (3 of 4)
Kerberos is a cross-platform authentication protocol that uses key encryption to verify identity of clients and to securely exchange information after a client logs on to a system
Kerberos is an example of S S O (single sign-on)
The most popular A A A service is RADIUS (Remote Authentication Dial-In User Service)
T A C A C S+ (Terminal Access Controller Access Control System Plus) offers network administrators the option of separating the access, authentication, and auditing capabilities
W E P offered two forms of authentication, neither of which is secure: O S A (Open System Authentication) and S K A (Shared Key Authentication)

## Slide 66: Chapter Summary (4 of 4)
T K I P was a quick fix, designed more as an integrity check for W E P transmissions than as a sophisticated encryption protocol
C C M P improves wireless security for newer devices that can use W P A2
The Personal versions of W P A and W P A2 are sometimes referred to as W P A-P S K
The Enterprise versions of W P A and W P A2 implement additional security measures