## Slide 1: Network+ Guide to Networks Eighth Edition
Chapter 12
Wide Area Networks
© 2019 Cengage. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Objectives
12.1 Identify the fundamental elements of WAN service options
12.2 Compare and contrast Layer 1 WAN technologies
12.3 Compare and contrast Layer 2 WAN technologies
12.4 Explain the most common wireless WAN technologies

## Slide 3: WAN Essentials (1 of 2)
WAN
  Network traversing significant distance, connecting LANs
Type of WAN needed depends upon:
  Traffic load
  Budget
  Geographic breadth
  Commercially available technology

## Slide 4: WAN Essentials (2 of 2)
WAN and LAN differences:
  LANs connect nodes; WANs connect networks spread over wide geographic area
  Both LANs and WANs use the same protocols from Layer 3 and higher
  Differ at Layers 1 and 2 access methods, topologies, and media
  LAN wiring: privately owned
  WANs: owned and operated by telcos (telecommunications carriers), also known as NSPs (network service providers)
    Examples: AT&T, Verizon, Charter, and Comcast

## Slide 5: Data Transfer Methods (1 of 4)
WAN link
  Connection between one WAN site (endpoint) and another site
  Can be point-to-point (one site to only one site) or multipoint (one site to two or more other sites)

## Slide 6: Data Transfer Methods (2 of 4)
Data terminal equipment (D T E)
  Customer’s endpoint device on the WAN
  Communicates on the LAN
Data communications equipment (D C E)
  Carrier’s endpoint device for the WAN
  Communicates on the WAN

## Slide 7: Data Transfer Methods (3 of 4)
Primary categories of WAN connections:
  Dedicated line—A cable or other telecommunications path has continuously available communications channels and is not shared with other users
  Virtual circuit—WAN connection logically appears to the customer to be dedicated, but, physically can be any configuration through the carrier’s cloud
    P V C (permanent virtual circuit)
    S V C (switched virtual circuit)
Switching determines how connections are created between nodes on a network
  Circuit-switched—Connection is established between two nodes before they begin transmitting data
  Packet-switched—Data is broken into packets before it’s transported

## Slide 8: Data Transfer Methods (4 of 4)
Table 12-1 Overview of wired WAN technologies
Functions at O S I Layer 1 | Functions at O S I Layer 2 | Primary media
Dial-up over P S T N | PPP | Copper
I S D N over P S T N | PPP or frame relay | Copper
D S L | PPP, Ethernet, or A T M | Copper or fiber optic
Cable broadband | Cable broadband, Ethernet | Copper and fiber optic
Metro Ethernet | Ethernet, M P L S | Copper, fiber optic, or wireless
T-carriers | PPP, frame relay, or A T M | Copper or fiber optic
SONET | PPP, frame relay, A T M, M P L S | Fiber-optic

## Slide 9: Troubleshooting an Internet Connection (1 of 2)
There are steps to take when troubleshooting a problem with a WAN connection
  Before calling your I S P
Preventative measures can be implemented to avoid having the problem in the first place
Need to know the difference between I S P’s equipment and subscriber’s equipment located at the customer’s premises, regardless of who owns it and who is responsible, is called customer premise equipment (C P E)
Equipment belonging to the ISP should only be serviced by the I S P’s technicians
  Even if located on the customer’s side of demark (demarcation point)

## Slide 10: Troubleshooting an Internet Connection (2 of 2)
Devices commonly found at or near the demarc:
  N I U (network interface unit)
    Smart jack—A more intelligent version of an N I U and can provide diagnostic information
  Line driver
  C S U/D S U
Common issues to look for:
  Interface error
  D N S issues
  Router misconfiguration
  Interference

## Slide 11: Layer 1 WAN Technologies
Physical layer services are generally performed by Layer 1 standards such as:
  D S L, I S D N, SONET, and T-carrier links
Broadband:
  Cables and bandwidth are shared between multiple customers
  I S P makes a “best effort” attempt to provide up to advertised bandwidth
  Bandwidth is asymmetrical (asynchronous)
    Download speeds are faster than upload speeds
D I A (dedicated internet access):
  Dedicated to a single customer
  Bandwidth is symmetrical (synchronous)
    Download and upload speeds are the same
    Important for businesses that back up large amounts of data online

## Slide 12: P S T N (Public Switched Telephone Network) (1 of 3)
P S T N (public switched telephone network):
  Circuit-switching network of lines, carrier equipment providing telephone service
  Also called P O T S (plain old telephone service)
  Originally: Analog traffic
  Today: Digital data, computer controlled switching
C O (central office):
  Where telephone company terminates lines
  Switches calls between different locations

## Slide 13: P S T N (Public Switched Telephone Network) (2 of 3)
Local loop (last mile)
  Portion of the P S T N connecting residence or business to nearest CO
N I U (network interface unit)
  Termination point at customer’s demarcation point
Three examples of P S T N-based network technologies:
  Dial-up
  I S D N
  D S L
Dial-up and I S D N are mostly obsolete
  Important building-blocks for understanding later technologies

## Slide 14: P S T N (Public Switched Telephone Network) (3 of 3)

## Slide 15: D S L (Digital Subscriber Line) (1 of 4)
Operates over P S T N
Directly competes with cable broadband and T1 services
Requires repeaters for longer distances
Distance between the customer and C O affect actual throughput
Supports multiple data, voice channels
  Over a single line
Uses advanced data modulation techniques:
  Data signal alters carrier signal properties
  Amplitude or phase modulation

## Slide 16: D S L (Digital Subscriber Line) (2 of 4)
Types of D S L
  X D S L refers to all D S L varieties
Better-known D S L varieties:
  A D S L (asymmetric D S L)—Faster download speeds than upload speeds
    Most common form of D S L
    Best use: video conferencing, web surfing
  V D S L (very high bit rate D S L or variable D S L)
    Faster than ADSL and also asymmetric
  S D S L (symmetric D S L)—Has equal download and upload speeds maxing out around 2 Mbps
    Best use: uploading, downloading significant data amounts

## Slide 17: D S L (Digital Subscriber Line) (3 of 4)
D S L equipment

## Slide 18: D S L (Digital Subscriber Line) (4 of 4)
Path of an A D S L connection:
  Establish T C P connection
  Transmit through D S L modem:
    Internal or external
    Splitter separates incoming voice, data signals
    May connect to switch or router
  D S L modem forwards modulated signal to local loop:
    Signal continues over four-pair U T P wire
    Distance less than 18,000 feet: signal combined with other modulated signals in telephone switch
  Carrier’s remote switching facility:
    Splitter separates data signal from voice signals
    Request sent to D S L A M (D S L access multiplexer)
    Request issued from carrier’s network to Internet backbone

## Slide 19: Cable Broadband (1 of 3)
Cable companies connectivity option
Based on coaxial cable wiring used for TV signals
Standardized by an international cooperative effort
  Suite of specifications called D O C S I S (Data Over Cable Service Interface Specifications)
Typically offered at asymmetric speeds
  Up to 70 Mbps download and 7 Mbps upload
Newest D O C I S standard 3.1 allows for full duplex or symmetric speeds
  Up to 10 Gbps in both directions
Best uses
  Web surfing or network data download

## Slide 20: Cable Broadband (2 of 3)
Many cable companies employ fiber cabling for a significant portion of their physical infrastructure
H F C (hybrid fiber coaxial) network use fiber-optic cabling to connect the cable company’s distribution center, to distribution hubs and then to optical nodes near customers

## Slide 21: Cable Broadband (3 of 3)
Cable modem:
  Modulates, demodulates transmission, reception signals via cable wiring
  Operates at Physical and Data Link layers
  May connect to connectivity device
Provides dedicated connection
Many subscribers share same local line, throughput

## Slide 22: Metro (Metropolitan) Ethernet (1 of 3)
Metro Ethernet Forum (M E F):
  An alliance of over 220 industry organizations worldwide
  Developing ways to send Ethernet traffic across MAN and WAN connections
Carrier-Ethernet Transport (C E T)
  An Ethernet-based transport solution designed to overcome weaknesses of implementing Ethernet outside the LAN environment

## Slide 23: Metro (Metropolitan) Ethernet (2 of 3)

## Slide 24: Metro (Metropolitan) Ethernet (3 of 3)
Metro Ethernet advantages:
  Streamlined connections
  Cost efficiency
  Scalability
  Familiarity
  Hardware

## Slide 25: T-Carriers (1 of 5)
T-carrier technology includes:
  T1s, fractional T1s, and T3s
AT&T developed T-carrier technology in 19 57
Medium
  Specially conditioned copper wire, fiber-optic cable, and wireless links

## Slide 26: T-Carriers (2 of 5)
Types of T-carrier lines
  T1—Connects branch offices, connects to carrier
    T-carrier standards (T-C X R standards) uses T D M (time division multiplexing) over two wire pairs to divide a single channel into multiple channels
  T3—Provides 28 times more throughput than a T1
    More expensive than T1s
    Used by more data-intensive businesses
  Fractional T1—Allows organizations to use only some of the channels on a T1 line
    Charged according to the number of channels they use

## Slide 27: T-Carriers (3 of 5)
Voice services optimization—T1s support voice services in two ways:
  I S D N P R I—T1 line with channels slightly reorganized
  S I P (Session Initial Protocol) trunk
    S I P trunking employs VoIP to create virtual connections over an existing data service
T-carrier equipment

## Slide 28: T-Carriers (4 of 5)
T-carrier equipment (continued)
  Smart jack—Terminates a T-carrier line at the customer’s demark and functions as a monitoring point for the connection
  C S U/D S U—Serves as the D T E (data terminal equipment) or endpoint device for a leased line
    C S U provides termination for the digital signal
    D S U converts T-carrier frames into frames the LAN can interpret (and vice versa)
  Multiplexer—Combines multiple signals from a LAN for transport over the T-carrier line
    Separates an incoming T-carrier line’s combined channels into individual signals that can be interpreted

## Slide 29: T-Carriers (5 of 5)

## Slide 30: SONET (Synchronous Optical Network) (1 of 4)
SONET—A high-bandwidth WAN signaling technique
Key strengths:
  WAN technology interoperability
  Fast data transfer rates
  Simple link additions, removals
  High degree of fault tolerance (self-healing)
Considered the best choice for linking WANS between North America, Europe, and Asia
Internationally, SONET is known as S D H (Synchronous Digital Hierarchy)

## Slide 31: SONET (Synchronous Optical Network) (2 of 4)
SONET often traverses multiple ISP networks
  Connecting networks through the Internet backbone
On the transmitting end, SONET multiplexers accept input from different network types
  Format the data in a standard SONET frame
Multiplexer combines individual SONET signals on the transmitting end
  A demultiplexer on the receiving end separates combined signals and translates incoming signals back into their original form

## Slide 32: SONET (Synchronous Optical Network) (3 of 4)

## Slide 33: SONET (Synchronous Optical Network) (4 of 4)
SONET’s transmissions rely on a timing scheme
  Frames will travel without data rather than disrupt the schedule
SONET frames are a consistent size
  Include information indicating where the payload begins
Data rate of a SONET connection is indicated by its O C (Optical Carrier) level
Commonly used by:
  Large companies
  Long-distance companies linking metropolitan areas and countries
  I S Ps that want to guarantee fast, reliable access to the Internet
  Telephone companies connecting their C Os

## Slide 34: Layer 2 WAN Technologies
Some Layer 2 technologies do traverse the I S P’s network
  In order to connect two or more LANs across a WAN connection
Three technologies:
  Frame relay
  A T M (Asynchronous Transfer Mode)
  M P L S (multiprotocol label switching)

## Slide 35: Frame Relay (1 of 3)
Frame relay:
  Group of Layer 2 protocols originally designed as a fast packet-switched network over I S D N
  Today is used as the Data Link protocol for various circuit interfaces and media
Data-link connection identifier (D L C I)
  Identifier routers read to determine which circuit to use for the frame
Frame relay is a connection-oriented protocol

## Slide 36: Frame Relay (2 of 3)

## Slide 37: Frame Relay (3 of 3)
P V C (permanent virtual circuit)
  Connections established before data needs to be transmitted and are maintained after transmission
Advantage:
  Pay for only the amount of bandwidth required
  Less expensive than other WAN technologies

## Slide 38: A T M (Asynchronous Transfer Mode) (1 of 3)
Functions at the Data Link layer
Asynchronous communications method:
  Nodes do not conform to predetermined schemes
    Specifying data transmissions timing
  Each character transmitted
    Start and stop bits
Specifies Data Link layer framing techniques
Fixed packet size
  Packet (cell)
    48 data bytes plus 5-byte header

## Slide 39: A T M (Asynchronous Transfer Mode) (2 of 3)
Smaller packet size requires more overhead:
  Decrease potential throughput
  Cell efficiency compensates for loss
A T M relies on virtual circuits:
  A T M considered packet-switching technology
  Virtual circuits provide circuit switching advantage
  Reliable connection
Allows specific Q o S (quality of service) guarantee
  Important for time-sensitive applications

## Slide 40: A T M (Asynchronous Transfer Mode) (3 of 3)

## Slide 41: M P L S (Multiprotocol Label Switching) (1 of 2)
M P L S:
  Enables multiple types of Layer 3 protocols to travel over any one of several connection-oriented Layer 2 protocols
  Can handle various types of payloads
  Often used by I S Ps on their own networks for moving traffic from one customer site to another
  Can use packet-switched technologies over traditionally circuit-switched networks
  M P L S labels include information about where the router should forward the message next
    Include prioritization information

## Slide 42: M P L S (Multiprotocol Label Switching) (2 of 2)

## Slide 43: Wireless WANs
Wireless WANS
  Specifically designed for high-throughput; long-distance digital data exchange

## Slide 44: Cellular (1 of 4)
Initially designed for analog phone service
  Today it can deliver data and voice
Cellular technology generations:
  1G: analog
  2G: digital transmission up to 240 Kbps
  3G: data rates up to 384 Kbps
    Data communications use packet switching
  4G: all-I P, packet switched network for data and voice
    Specifies throughputs of 100 Mbps for fast-moving clients; 1 Gbps for slow-moving clients
  5G: don’t exist yet
    Expect 5G devices to offer download speeds of up to 20 Gbps and upload speeds of 10 Gbps

## Slide 45: Cellular (2 of 4)
Use one of two competing voice technologies:
  G S M (Global System for Mobile Communications)
  C D M A (Code Division Multiple Access)
Network infrastructure:
  Cells served by antenna and base station
  Controller assigns mobile clients frequencies
Cell size depends on:
  Network’s access method
  Region’s topology, population, and amount of cellular traffic

## Slide 46: Cellular (3 of 4)

## Slide 47: Cellular (4 of 4)
M S C (Mobile switching center)
  Also called an M T S O
Each base station is connected to an M S C by a wireless link or fiber-optic cabling (see Figure 12-27 on previous slide)
Basic infrastructure:
  H S P A+ (High Speed Packet Access Plus)
    3G technology
  L T E (Long-Term Evolution)
    4G technology

## Slide 48: Satellite (1 of 4)
Originally used to transmit telephone and television signals across the Atlantic Ocean
Today, satellites are used for transmitting consumer voice, video, music, and data
Satellite orbits:
  Geosynchronous Earth orbit (G E O)
    Satellites orbit at same rate Earth turns
    Most popular
  Uplink/Downlink
    Satellite transponder transmits signal to Earth-based transmitter
  Typical satellite
    24–32 transponders
    Unique downlink frequencies
  Frequencies, as well as satellite’s orbit location are assigned and regulated by the F C C

## Slide 49: Satellite (2 of 4)

## Slide 50: Satellite (3 of 4)
Satellites transmit and receive signals in any of six frequency bands
Within each band, frequencies used for uplink and downlink differ
Table 12-5 Satellite frequency bands
Band | Frequency range
L-band | 1.5-2.7 GHz
S-band | 2.7-3.5 GHz
C-band | 3.4-6.7 GHz
Ku (“K-under band”) | 12-18 GHz
K-band | 18-27 GHz
Ka-band (“K-above band”) | 26.5-40 GHz

## Slide 51: Satellite (4 of 4)
Satellite Internet services:
  Subscriber uses small satellite dish antenna, receiver, or satellite modem
  Exchanges signals with provider’s satellite network
  Typically asymmetrical
  Bandwidth shared among many subscribers
  Throughput controlled by service provider
  Typical downlink rates range from 2 to 3 Mbps
    Uplink rates may reach 1 Mbps

## Slide 52: Chapter Summary (1 of 4)
A proxy server acts as an intermediary between the external and internal networks
Thanks to a router’s A C L or access list, routers can decline to forward certain packets depending on their content
A firewall is a specialized device or software that selectively filters or blocks traffic between networks
An I D S (intrusion detection system) is a stand-alone device, an application, or a built-in feature running on a workstation, server, switch, router, or firewall, which is used to monitor network traffic
I D S, I P S, firewalls, and proxy servers all generate a great deal of data that is stored in logs and must be monitored and analyzed

## Slide 53: Chapter Summary (2 of 4)
S T P (Spanning Tree Protocol) prevents traffic loops by calculating paths that avoid potential loops and blocking links that would complete a loop
Unused physical and virtual ports on switches and other network devices should be disabled until needed
Controlling users’ access to a network consists of three major elements: authentication, authorization, and accounting
With geofencing, G P S or R F I D data is sent to the authentication server to report the location of the device attempting to authenticate to the network
Systems generate many logs that can be used for troubleshooting and auditing
A N A C system employs a set of rules, called network policies, which determine the level and type of access granted to a device when it joins a network

## Slide 54: Chapter Summary (3 of 4)
Kerberos is a cross-platform authentication protocol that uses key encryption to verify identity of clients and to securely exchange information after a client logs on to a system
Kerberos is an example of S S O (single sign-on)
The most popular A A A service is RADIUS (Remote Authentication Dial-In User Service)
T A C A C S+ (Terminal Access Controller Access Control System Plus) offers network administrators the option of separating the access, authentication, and auditing capabilities
W E P offered two forms of authentication, neither of which is secure: O S A (Open System Authentication) and S K A (Shared Key Authentication)

## Slide 55: Chapter Summary (4 of 4)
T K I P was a quick fix, designed more as an integrity check for W E P transmissions than as a sophisticated encryption protocol
C C M P improves wireless security for newer devices that can use W P A2
The Personal versions of W P A and W P A2 are sometimes referred to as W P A-P S K
The Enterprise versions of W P A and W P A2 implement additional security measures